| Stuart Petroleum Limited | BAZZARD-1 |
| --- | --- |
| Report Date: | 03 October 2008 | Bit Diameter: | 311.1 mm (12.25”) |
| Report Number: | 11 | Last Casing: | 399 mm (13-3/8”) @ 841 m |
| Spud Date: | 20 September 2008 | LOT: | 15.06 ppg at 853m |
| Days from Spud: | 12 | Mud Weight: | 9.5 |
| Current Activity (06:00 hours): | RIH at 2220m. | ECD: | - |
| Water Depth: | 68 m | Mud Type: | KCl / PHPA |
| Rotary Table: | 38.5 m above AHD. | Last Survey: | 2846.49m incl 0.04° azim 239.3° |

| Time / Date | m MDRT | m TVDRT | Previous, m | Progress, m | Drill rate m/hr |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Minimum | Maximum | Average |
| 06:00 hrs, 02/10/08 | 2859 |  | 2859 | 0 | - | - | - |

| Depth m MDRT | Description | Gas Data (total gas in %; C1, C2, C3, iC4, nC4, iC5, nC5 in ppm), C1/2/3/4/5/ ratios indicated below. |
| --- | --- | --- |
|  | No new formation drilled |  |

| Depth m MDRT | Fluorescence | Cut | Residue ring / film |
| --- | --- | --- | --- |

| (m MDRT) | Total Gas (%) | Methane (ppm) | Ethane (ppm) | Propane (ppm) | i-Butane (ppm) | n-Butane (ppm) | i-Pentane (ppm) | n-Pentane (ppm) | % Ratios (C1/2/3/4/5) | Type |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

KEY: BG Background gas, CG Connection gas,   POG Pumps-off gas, TG Trip gas, STG Short trip gas, FMG Formation gas

| From m MDRT | To m MDRT | Total or Rate (bbl) | Remarks |
| --- | --- | --- | --- |
|  |  |  | No losses recorded during tripping. |

Run 2 MWD / LWD string as follows: Resistivity: 3.98m, ARC Gamma 4.03m, D&I (survey) 11.54m, Sonic 21.01m, SADN Density 25.51m, SADN Porosity 28.37m Source removed 06:45 – 07:10 hrs Tool all out of hole 09:00 hrs, end Run 2 Run 2 MWD / LWD string as follows: Resistivity: 3.97m, ARC Gamma 4.02m, D&I (survey) 11.53m, Sonic 20.98m, SADN Density 26.92m, SADN Porosity 28.90m Using Powerpulse MWD. Commence pickup tool 09:00 Load source 11:00-11:35 RIH 11:35-12:30 Shallow test. 12:45-13.00 Tools failed to transmit RT data Pulled BHA 14:30 Diagnosis of RT connection faults on tools 14:30-16:30 RIH 16:30-17:00 Shallow test 17:00 All tools with the exception of the SADN transmitting RT data RIH 18:20 (maintenance done on top drive ~17:30-18:10, 04:00-05.15) No specific data acquisition required while running in hole. Run 2 RM data processed as follows: Gamma / resistivity log 850-2855m, gamma trace corrected for KCl in mud. SADN Density / Neutron data 850-2200m. Sonic data 850-2600m preprocessed for transmittal to SLB DCS for final processing.

| Formation (Unit) | Prognosed MDRT SS, m | Actual MDRT TVDSS, m | Actual Thickness | Difference to Prog (TVDSS) | Basis Of Pick |
| --- | --- | --- | --- | --- | --- |
| Gippsland Limestone | 106 | -68 | 106.5 | -68 | 1803.4 | 0 | Sea-floor |
| Lakes Entrance | 1918.5 | -1880 | 1910 | -1871.4 | 189.8 | -8.6 | Slight increase in gamma, subtle change in cuttings |
| Latrobe Group: |  |  |  |  |  |  |  |
| Gurnard Formation | 2097.5 | -2059 | 2010 | -2061.2 | 27 | +2.2 | Greensand in cuttings |
| Kingfish Formation | 2132.5 | -2094 | 2127 | -2088.2 |  | -5.8 | Drill break, coarse quartz sand in cuttings |
| 54-5 Sand | 2513.5 | -2475 | 2537? | -2497.9 |  | +22.9 | Drill break, low gamma interval |
| 62 Sand | 2798.5 | -2760 | 2789? | -2749.9 |  | -10.1 | Drill break, coarse quartz sand in cuttings |
| Volador Fm 66.5 Sand | 2978.5 | -2940 |  |  |  |  |  |
| 67 Sand | 3218.5 | -3180 |  |  |  |  |  |
| 70 Sand | 3438.5 | -3400 |  |  |  |  |  |
| TD | 3501.5 | -3463 |  |  |  |  |  |

Tight intervals requiring washing and reaming through at 1395m, 1497m, 1953m, 2131-2220m. Mudlog updated with RM log curve for resistivity.

Geologists:  Simon Ward / Roman Leslie

# Text boxes

Lithology Summary:

Drilling Summary:

Oil Fluorescence Summary:

Gas Summary:

Fluid Loss:

MWD Summary:

Wellsite Formation Picks:

Comments: