| Stuart Petroleum Limited | BAZZARD-1 |
| --- | --- |
| Report Date: | 30 September 2008 | Bit Diameter: | 311.1 mm (12.25”) |
| Report Number: | 8 | Last Casing: | 399 mm (13-3/8”) @ 841 m |
| Spud Date: | 20 September 2008 | LOT: | 15.06 ppg at 853m |
| Days from Spud: | 9 | Mud Weight: | 9.5 |
| Current Activity (06:00 hours): | Drilling 311 mm (12-1/4”) hole. | ECD: | 9.9 |
| Water Depth: | 68 m | Mud Type: | KCl / PHPA |
| Rotary Table: | 38.5 m above AHD. | Last Survey: | 2492.88m incl 1.55° azim 355.74° |

| Time / Date | m MDRT | m TVDRT | Previous, m | Progress, m | Drill rate m/hr |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Minimum | Maximum | Average |
| 06:00 hrs, 30/09/08 | 2504 | 2503.7 | 2082 | 422 | 13.7 | 75.2 | 39.5 |

| Depth m MDRT | Description | Gas Data (total gas in %; C1, C2, C3, iC4, nC4, iC5, nC5 in ppm), C1/2/3/4/5/ ratios indicated below. |
| --- | --- | --- |
| 2060-2100 | CALCILUTITE (35-60%): light olive grey to light grey, soft to firm, subblocky, common clastic silt and clay. CLAYSTONE (35-60%): medium light grey to medium grey, moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately to highly calcareous. Trace forams. SILTSTONE (5-10%): medium grey to greenish grey, firm to hard, blocky, argillaceous, moderately to highly calcareous. Trace black carbonaceous laminae. | 0.10, 762/19/14/3/2/1/0 95/2/2/1/0 |
| 2100-2127 | GURNARD FORMATION: CLAYSTONE (30-40%): medium light grey to medium grey, moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately to highly calcareous, trace forams. CALCILUTITE (10-20%): light olive grey to light grey, soft to firm, subblocky, common clastic silt and clay. GLAUCONITIC SANDSTONE (20%): white to light grey to greenish grey, firm to hard, blocky, very fine to medium, moderately sorted, subangular quartz and common dark green fine to medium grained subangular to well rounded glauconite in a firm to hard silty matrix with calcareous cement, poor visible porosity. Common loose glauconite grains. SILTSTONE (10-20%): moderate olive brown, very soft, dispersive, argillaceous, glauconitic in parts, non calcareous. SILTSTONE (10-20%): medium grey to greenish grey, firm to hard, blocky, argillaceous, moderately to highly calcareous. Trace black carbonaceous laminae. | 0.09, 656/31/21/2/2/1/0 92/4/3/1/0 |

| 2127-2280 | KINGFISH FORMATION: SANDSTONE (40-100%): white to light grey to yellowish grey to moderate yellow, loose and occasional aggregates (of fine sst ± coal), fine, medium and coarse to granule (2.5mm), moderately to well sorted, subrounded to rounded, subspherical translucent to frosted quartz, in places broken, trace loose fine to granule sized pyrite, trace pyritised quartz. SILTSTONE (0-40%): moderate olive brown to dark grey, firm to hard, argillaceous to carbonaceous, non calcareous. CLAYSTONE (0-30%): light to medium grey, moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately calcareous. COAL (5-10% at 2200-2220m): dark brown to black, moderately hard to hard, angular, planar to conchoidal fractures. | 0.08, 481/31/29/3/6/1/1 87/6/5/2/0 |
| --- | --- | --- |
| 2280-2290 | CLAYSTONE (75%): light to medium grey, moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately calcareous. SILTSTONE (25%): moderate olive brown to dark grey, firm to hard, argillaceous to carbonaceous, non calcareous. Trace sandstone. Trace coal. | 0.13, 680/88/74/8/14/2/1 78/10/9/3/0 |
| 2290-2340 | SANDSTONE (45-85%): white to light grey, loose, medium and coarse to granule (2.5mm), moderately to well sorted, subrounded to rounded, subspherical translucent to frosted quartz, in places broken. SILTSTONE (0-40%): moderate olive brown to dark grey, firm to hard, argillaceous to carbonaceous, non calcareous. CLAYSTONE (5-15%): light to medium grey, moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately calcareous. COAL (5-35%): dark brown to black, hard, angular, planar to conchoidal fractures. | 0.15, 868/99/63/6/12/2/1 83/9/6/2/0 |
| 2340-2398 | SILTSTONE (10-85%): moderate olive brown to dark grey, firm to hard, argillaceous to carbonaceous, non calcareous. CLAYSTONE (10-75%): light to medium grey, moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately calcareous SANDSTONE (5-10%, 50% at 2380m): greyish yellow to moderate olive brown aggregates of very fine (silca cemented) sand, well sorted, with minor white to light grey, loose, medium and coarse to granule (2.5mm), moderately sorted, subrounded to rounded, subspherical translucent to frosted quartz, in places broken. COAL (tr, 10% at 2380m): dark brown to black, hard, angular, planar to conchoidal fractures. | 0.17, 861/113/76/7/14/2/1 80/11/7/2/0 |
| 2398-2415 | SANDSTONE (50%): light to medium grey loose fine lower to coarse lower, dominantly medium sand, poorly sorted, subangular to subrounded clear to frosted quartz, broken in parts, trace crystalline pyrite, trace quartz granules, trace brown grey very fine hard silty sandstone, trace calcareous medium sandstone. SILTSTONE (40-45%): moderate olive brown to dark grey, firm to hard, argillaceous to carbonaceous, non calcareous, trace coal fragments. CLAYSTONE (5-10%): light to medium grey, moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately calcareous. | 0.11, 485/54/59/6/13/2/2 79/9/9/3/1 |
| 2415-2455 | SILTSTONE (80%): moderate olive brown to medium grey, firm to hard, argillaceous to carbonaceous, non calcareous, trace coal fragments. Minor to pale grey firm slightly sandy siltstone, trace mica flakes, trace carbonaceous laminae. SANDSTONE (10%): light to medium grey loose fine lower to coarse upper, dominantly fine to medium sand, poorly to moderately sorted, subangular to subrounded clear to frosted quartz, broken in parts, trace crystalline pyrite, trace quartz granules. From 2440m, SILTSTONE grading to SANDSTONE (40-50%): light to medium brownish grey, firm to moderately hard, very fine lower, well sorted subangular quartz and trace mica in silty matrix, weakly cemented, common carbonaceous laminae. CLAYSTONE (10%): light to medium grey, moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately calcareous. | 0.17, 846/108/68/8/14/2/2 81/10/7/2/0 |
| 2455-2485 | SANDSTONE (20-80%): light to medium brownish grey, firm to moderately hard, very fine lower sandstone, well sorted subangular quartz and trace mica in silty matrix, weakly cemented, common carbonaceous laminae. Below 2460m, becoming white to light grey, loose, fine to coarse, trace granule, dominantly medium, well sorted, subrounded to rounded, subspherical translucent to frosted quartz, in places broken. Common soft white to light grey amorphous non-calcareous rockflour, inferred to be from sandstone matrix. Trace pyrite clusters and cemented grains. SILTSTONE (40-70%): moderate olive brown to medium grey, firm to hard, argillaceous to carbonaceous, non calcareous, trace coal fragments. Minor to common pale grey firm slightly sandy siltstone, trace mica flakes, trace carbonaceous laminae. CLAYSTONE (5-10%): light to medium grey, moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately calcareous. | 0.13, 695/60/61/7/12/2/2 83/7/7/2/1 |

| Depth m MDRT | Fluorescence | Cut | Residue ring / film |
| --- | --- | --- | --- |
| 2220-2225 | Trace moderately bright yellow-green patchy fluorescence from visible black liquid bitumen in silty very fine sandstone. | Very fast streaming bright greenish white cut fluorescence. | Wide spotty bright green-yellow fluorescing residual ring, pale brown visible residue. |
| 2375-2380 | Trace moderately bright green-yellow pinpoint fluorescence in siltstone. | Slow blooming dull blue-white cut fluorescence. | Pale blue-green moderately wide spotty fluorescing residual ring, nil visible residue. |
| 2405-2440 | Trace (2% at 2430m) dull to moderately bright pinkish yellow pinpoint fluorescence in fine sandstone aggregates. | Slow (fast at 2425m) blooming dull to moderately bright blue-white cut fluorescence. | Thin dull to moderately bright blue-white fluorescing residual rings, nil visible residue. |
| 2465-2470 | 2% dull yellow orange pinpoint fluorescence in siltstone | Moderately fast blooming dull blue white cut fluorescence. | Thin dull to moderately bright blue-white fluorescing residual ring, nil visible residue. |

| (m MDRT) | Total Gas (%) | Methane (ppm) | Ethane (ppm) | Propane (ppm) | i-Butane (ppm) | n-Butane (ppm) | i-Pentane (ppm) | n-Pentane (ppm) | % Ratios (C1/2/3/4/5) | Type |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2060-2100 | 0.10 | 462 | 19 | 14 | 3 | 2 | 1 | 0 | 92/4/3/1/0 | BG |
| 2100-2127 | 0.09 | 656 | 31 | 21 | 2 | 2 | 1 | 0 | 92/4/3/1/0 | BG |
| 2127-2504 | 0.12 | 671 | 69 | 52 | 6 | 10 | 2 | 1 | 83/9/6/2/0 | BG |

KEY: BG Background gas, CG Connection gas,   POG Pumps-off gas, TG Trip gas, STG Short trip gas, FMG Formation gas

| From m MDRT | To m MDRT | Total or Rate (bbl) | Remarks |
| --- | --- | --- | --- |
|  |  |  | Normal surface fluid losses only. |

Run 2 MWD / LWD string as follows: Resistivity: 3.98m, ARC Gamma 4.03m, D&I (survey) 11.54m, Sonic 21.01m, SADN Density 25.51m, SADN Porosity 28.37m LWD RT data quality poor to absent in places due to faulty upper standpipe pressure sensor and drilling noise, generally better below 2300m due to lower ROP. RT data gap 2444-2464m due to surface signal loss.

| Formation (Unit) | Prognosed MDRT SS, m | Actual MDRT TVDSS, m | Actual Thickness | Difference to Prog (TVDSS) | Basis Of Pick |
| --- | --- | --- | --- | --- | --- |
| Gippsland Limestone | 106 | -68 | 106.5 | -68 | 1803.4 | 0 | Sea-floor |
| Lakes Entrance | 1918.5 | -1880 | 1910 | -1871.4 | 189.8 | -8.6 (ie high) | Slight increase in gamma, subtle change in cuttings |
| Latrobe Group: |  |  |  |  |  |  |  |
| Gurnard Formation | 2097.5 | -2059 | 2010 | -2061.2 | 27 | +2.2 (low) | Greensand in cuttings |
| Kingfish Formation | 2132.5 | -2094 | 2127 | -2088.2 |  | -5.8 (high) | Drill break, coarse quartz sand in cuttings |
| 54-5 Sand | 2513.5 | -2475 |  |  |  |  |  |
| 62 Sand | 2798.5 | -2760 |  |  |  |  |  |
| Volador Fm 66.5 Sand | 2978.5 | -2940 |  |  |  |  |  |
| 67 Sand | 3218.5 | -3180 |  |  |  |  |  |
| 70 Sand | 3438.5 | -3400 |  |  |  |  |  |
| TD | 3501.5 | -3463 |  |  |  |  |  |

5m samples from 2200m.

Geologists:  Simon Ward / Roman Leslie

# Text boxes

Lithology Summary:

Drilling Summary:

Oil Fluorescence Summary:

Gas Summary:

Fluid Loss:

MWD Summary:

Wellsite Formation Picks:

Comments: