| Stuart Petroleum Limited | BAZZARD-1 |
| --- | --- |
| Report Date: | 01 October 2008 | Bit Diameter: | 311.1 mm (12.25”) |
| Report Number: | 9 | Last Casing: | 399 mm (13-3/8”) @ 841 m |
| Spud Date: | 20 September 2008 | LOT: | 15.06 ppg at 853m |
| Days from Spud: | 10 | Mud Weight: | 9.4 |
| Current Activity (06:00 hours): | Drilling 311 mm (12-1/4”) hole. | ECD: | 9.9 |
| Water Depth: | 68 m | Mud Type: | KCl / PHPA |
| Rotary Table: | 38.5 m above AHD. | Last Survey: | 2670.17m incl 0.61° azim 343.94° |

| Time / Date | m MDRT | m TVDRT | Previous, m | Progress, m | Drill rate m/hr |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Minimum | Maximum | Average |
| 06:00 hrs, 01/10/08 | 2712 | 2711.4 | 2504 | 208 | 1.7 | 80.5 | 19.5 |

| Depth m MDRT | Description | Gas Data (total gas in %; C1, C2, C3, iC4, nC4, iC5, nC5 in ppm), C1/2/3/4/5/ ratios indicated below. |
| --- | --- | --- |
| 2485-2500 | KINGFISH FORMATION (cont.): SILTSTONE (20-70%): moderate olive brown to medium grey, firm to hard, argillaceous to carbonaceous, non calcareous, trace coal fragments, minor pyrite. Common pale grey firm slightly sandy siltstone, trace mica flakes, trace carbonaceous laminae. SANDSTONE (20-70%): light to medium brownish grey, firm to moderately hard, very fine lower to upper sandstone, well sorted subangular quartz and trace mica in silty matrix, weakly cemented, common carbonaceous laminae. With minor loose very fine to medium sand, trace quartz granules. CLAYSTONE (10%): light to medium grey, soft to moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately calcareous. | 0.17, 1036/119/81/9/16/3/1.6 82/9/7/2/0 |
| 2500-2560 | SILTSTONE (50-90%): moderate olive brown to medium grey, firm to hard, argillaceous to carbonaceous, non calcareous, trace coal fragments, minor pyrite. Common pale grey firm slightly sandy siltstone, trace mica flakes, trace carbonaceous laminae. SANDSTONE (5-25%): light to medium brownish grey, firm to moderately hard, very fine lower to upper sandstone, well sorted subangular quartz and trace mica in silty matrix, weakly cemented, common carbonaceous laminae. With minor loose very fine to medium sand, trace quartz granules. CLAYSTONE (5%): light to medium grey, soft to moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately calcareous. COAL (Tr-30% at 2550-2555m): dark brown to black, hackly to conchoidal fracture. | 0.13, 689/61/52/8/10/2/1.4 84/8/6/2/0 |
| 2560-2590 | SILTSTONE (25-65%): moderate olive brown to medium grey, firm to hard, argillaceous to carbonaceous, non calcareous, trace coal fragments, minor pyrite. Common pale grey firm slightly sandy siltstone, trace mica flakes, trace carbonaceous laminae. SANDSTONE (Tr-45%): light to medium brownish grey, firm to moderately hard, very fine lower to upper sandstone, well sorted subangular quartz and trace mica in silty matrix, weakly cemented, common carbonaceous laminae. With minor loose very fine to medium sand, trace quartz granules. CLAYSTONE (20-40%): light to medium grey, soft to moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately calcareous. COAL (Tr-10%): dark brown to black, hackly to conchoidal fracture. | 0.12, 555/35/48/9/5/2/0 85/6/7/2/0 |
| 2590-2605 | SILTSTONE (50-60%): moderate olive brown to medium grey, firm to hard, argillaceous to carbonaceous, non calcareous, trace coal fragments, minor pyrite. Common pale grey firm slightly sandy siltstone, trace mica flakes, trace carbonaceous laminae. CLAYSTONE (15-35%): light to medium grey, soft to moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately calcareous. SANDSTONE (10-25%): light to medium brownish grey, firm to moderately hard, very fine lower to upper sandstone, well sorted subangular quartz and trace mica in silty matrix, weakly cemented, common carbonaceous laminae. With minor loose very fine to medium sand, trace quartz granules. COAL (Tr-5%): dark brown to black, hackly to conchoidal fracture. | 0.10, 405/19/42/8/4/2/3 84/4/9/2/1 |
| 2605-2620 | SANDSTONE (45-85%): white to very light grey, predominantly loose with occasional aggregates, medium (l-u) to coarse with minor granule, moderately to well sorted, subangular to subrounded clear to frosted quartz, trace pyrite, trace muscovite flakes. Trace coal. SILTSTONE (10-40%): moderate olive brown to medium grey, firm to hard, argillaceous to carbonaceous, non calcareous, trace coal fragments, minor pyrite. Common pale grey firm slightly sandy siltstone, trace mica flakes, trace carbonaceous laminae. CLAYSTONE (5-15%): light to medium grey, soft to moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately calcareous. COAL (Tr-5%): dark brown to black, hackly to conchoidal fracture. | 0.09, 316/5/30/5/7/2/0.8 86/2/8/3/1 |
| 2620-2675 | SILTSTONE (75-90%): moderate olive brown to medium grey, firm to hard, argillaceous to carbonaceous, non calcareous, trace coal fragments, minor pyrite. Trace to common pale grey firm slightly sandy siltstone, trace mica flakes, trace carbonaceous laminae. SANDSTONE (5-20%): very light grey to light to medium brownish grey, firm to moderately hard, very fine lower to upper sandstone, in parts trace fine sandstone , well sorted subangular quartz and trace mica in silty matrix, weakly silica cemented, common carbonaceous laminae. With common loose very fine to fine sand, minor medium sand, moderately sorted, subrounded, trace quartz granules. CLAYSTONE (5%): light to medium grey, moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately calcareous. | 0.11, 441/18/45/7/7/3/1 85/3/9/3/0 |
| 2675-2705 | SANDSTONE (50-60%, 20-30% below 2690m): White to pale grey loose very fine to coarse sand, dominantly fine to medium (fining downwards), moderately sorted, subrounded quartz. Common very light grey to light to medium brownish grey, firm to moderately hard, very fine lower to upper sandstone, well sorted subangular quartz and trace mica in silty matrix, weakly silica cemented. SILTSTONE (35-45%, 65-75% below 2690m): pale to moderate olive brown to medium grey, firm to hard, argillaceous to carbonaceous, non calcareous, trace coal fragments, minor pyrite. Trace pale grey firm slightly sandy siltstone, trace mica flakes. CLAYSTONE (5%): light to medium grey, moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately calcareous. | 0.12, 505/27/45/8/8/3/1 85/4/7/3/1 |

| Depth m MDRT | Fluorescence | Cut | Residue ring / film |
| --- | --- | --- | --- |
| 2535-2540 | Trace bright greenish yellow pinpoint fluorescence in calcareous claystone. | Slow blooming moderately bright blue-white cut fluorescence. | Thin dull blue white fluorescing residual ring, nil visible residue. |
| 2545-2550 | Trace bright greenish white pinpoint fluorescence in coal (resin). | Slow blooming moderately bright blue white cut fluorescence. | Wide bright blue green fluorescing residual ring, nil visible residue. |

| (m MDRT) | Total Gas (%) | Methane (ppm) | Ethane (ppm) | Propane (ppm) | i-Butane (ppm) | n-Butane (ppm) | i-Pentane (ppm) | n-Pentane (ppm) | % Ratios (C1/2/3/4/5) | Type |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2504-2712 | 0.12 | 623 | 33 | 46 | 8 | 8 | 3 | 1 | 86/5/6/2/1 | BG |

KEY: BG Background gas, CG Connection gas,   POG Pumps-off gas, TG Trip gas, STG Short trip gas, FMG Formation gas

| From m MDRT | To m MDRT | Total or Rate (bbl) | Remarks |
| --- | --- | --- | --- |
|  |  |  | Normal surface losses plus intermittent high losses on solid control equipment. No downhole losses. |

Run 2 MWD / LWD string as follows: Resistivity: 3.98m, ARC Gamma 4.03m, D&I (survey) 11.54m, Sonic 21.01m, SADN Density 25.51m, SADN Porosity 28.37m LWD RT data quality poor in places due to faulty upper standpipe pressure sensor and drilling noise to 2563m. Below 2563m, faulty sensor cable for upper standpipe pressure sensor replaced, good quality data recorded. Below 2605m, RT sonic data no longer available, recycling of pumps shows that tool no longer communicating. Intermittent signal received from ARC tool (gamma / resistivity), though good log data still being received. LWD engineers indicate that Sonic will be operating on battery only, with the expected battery life of c.12 hours from about midnight, therefore expect tool to cease functioning around midday 01 Oct. After recycling pumps at 01:00 hrs, ARC tool appears to be fully functional. Battery life in ARC anticipated to be about 48 hours from midnight. SADN battery expected to have been exhausted yesterday afternoon.

| Formation (Unit) | Prognosed MDRT SS, m | Actual MDRT TVDSS, m | Actual Thickness | Difference to Prog (TVDSS) | Basis Of Pick |
| --- | --- | --- | --- | --- | --- |
| Gippsland Limestone | 106 | -68 | 106.5 | -68 | 1803.4 | 0 | Sea-floor |
| Lakes Entrance | 1918.5 | -1880 | 1910 | -1871.4 | 189.8 | -8.6 | Slight increase in gamma, subtle change in cuttings |
| Latrobe Group: |  |  |  |  |  |  |  |
| Gurnard Formation | 2097.5 | -2059 | 2010 | -2061.2 | 27 | +2.2 | Greensand in cuttings |
| Kingfish Formation | 2132.5 | -2094 | 2127 | -2088.2 |  | -5.8 | Drill break, coarse quartz sand in cuttings |
| 54-5 Sand | 2513.5 | -2475 | 2537? | -2497.9 |  | +22.9 | Drill break, low gamma interval |
| 62 Sand | 2798.5 | -2760 |  |  |  |  |  |
| Volador Fm 66.5 Sand | 2978.5 | -2940 |  |  |  |  |  |
| 67 Sand | 3218.5 | -3180 |  |  |  |  |  |
| 70 Sand | 3438.5 | -3400 |  |  |  |  |  |
| TD | 3501.5 | -3463 |  |  |  |  |  |

Drill to 2563m, pull and rack back 11 stands, pick up 10 more stands and continue drilling to 2889m. Pick for 54-4 Sand unit to be confirmed by Operations Geologist.

Geologists:  Simon Ward / Roman Leslie

# Text boxes

Lithology Summary:

Drilling Summary:

Oil Fluorescence Summary:

Gas Summary:

Fluid Loss:

MWD Summary:

Wellsite Formation Picks:

Comments: