LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Boola Boola-2 | REPORT No. : | 20 | DFS: | 19 | DATE : | 20-06-07 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 1594.00m | LAST DEPTH : | 1556.00m | 24 HR PROGRESS: | 38.00m | PTD : | 1700 m |
| TOTAL FUEL : | 5800 | FUEL USAGE : | 3500 | DAYCOST : $ | 61,208 | CUM. COST : $ | 1,989,756 |
| 0600 OPS : | 0-0 - Con’t POH 0100 - M/U new bit RIH 0545 Obstruction @ 1390m – ream w/kelly |
| Next 24 Hrs Op | Finish RIH – Drill ahead |
| Site Personnel: | Dave Hair - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 8 | 7 Re-run |  | Drilling | 15.5 |  | Density | 1.128 | S.G. |
| Size (mm) | 216 | 216 |  | Tripping | 5 |  | Viscosity | 38 | Sec |
| Make | Reed | Reed |  | Surveys | .5 |  | Water Loss | 10.0 | Cc |
| Type | TD43AP | TD 51AP |  | Rigged up BOP |  |  | pH | 9.5 | Strip |
| IADC Code | 4-3-7 | 5-1-7 |  | Slip cut Line |  |  | Filter Cake | 1 | 32 nd |
| Serial Number | EM2047 | JK2076 |  | Circulate Sample |  |  | PV / YP | 12/ 14 | Cp/lb/100’ |
| Nozzles (32) | 12-12-12 | 12-12-12 |  | Casing |  |  | Gels | 6 / 11 | S/m |
| Depth in (m) | 1594 | 1415 |  | F.I.T |  |  | Sand | tr | % Vol |
| Depth out (m) |  | 1594 |  | Surveys |  |  | Solids | 7.5 | % Vol |
| Total Metres |  | 179 |  | Circulate & Condition | .5 |  | Oil |  | % Vol |
| Hours |  | 60 |  | Rig Service |  |  | K+ | 5,250 | Mg/l |
| WOB (kg) | 14 | 14 |  | Pick up BHA |  |  | Chlorides | 8,200 | Mg/l |
| RPM | 70 - 80 | 80 |  | Drill out Cmt |  |  | PHPA |  |  |
| Condition |  | 6-3-BT-M-E-2-LT-8-PR |  | Repair rig | 2.5 |  | KCL | 1.0 | % by wt |
| Impact Force |  | 565 |  | Wait On Cement |  |  | Daily Cost $ | 457.05 |
| Jet Velocity |  | 334 |  | Test BOPs |  |  | Cum Cost $ | 25,726.40 |
| B.H.A.: | 216mm Bit-Bit Sub-NMDC-1 x 6-1/4 DC-STB-15 x 6-1/4 DC-JARS-1 x 6-1/4 DC-4 HWDP |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 30 | ° at | 1486 | m |  | Type | Amount |
| 0000 | 0400 | Drilled 216mm hole from 1556 to 1568 |  | 25 | ° at | 1581 | m |  | Biocide | 1 |
| 0400 | 0630 | Genset shut down – l/d 5 jts – W/O fuel |  | 14 | ° at | 1076 | m |  | Sodium Sulphite |  |
| 0630 | 0730 | Run back to bottom |  | 20 | ° at | 1131 | m |  | Pac - R |  |
| 0730 | 1900 | Drill 1568 to 1594 |  | 23½ | ° at | 1186 | m |  | Barite | 25 |
| 1900 | 1930 | Circ shakers clean |  | 24 | ° at | 1206 | m |  | Xanthum gum |  |
| 1930 | 2000 | Run wireline survey @ 1581 – 25 Deg – Az 274 |  | 26 | ° at | 1281 | m |  | PHPA/ KCL |  |
| 2000 | 2400 | SCR – Pump slug – flow check – Pooh for bit change |  | 31 | ° at | 1354 | m |  | Caustic Soda | 1 |
|  |  |  |  | PUMP 1 |  | PUMP 2 |
|  |  |  |  | Liner | 108 | mm |  | Liner | 108 | mm |
|  |  |  |  | Pressure | 10,000 | kPa |  | Pressure | 10,000 | KPa |
|  |  |  |  | A.V. DP | 163 | f/min |  | A.V. DP |  | f/min |
|  |  |  |  | A.V. DC | 255 | f/min |  | A.V. DC |  | f/min |
|  |  |  |  | SPM | 85 |  | SPM | 85 |
|  |  | 2 loads of water used today Total 34 |  | GPM | 173 |  | GPM | 173 |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton | 50% Excess |  | Size | 244 | mm |
|  |  |  |  | Class Bulk | 506 |  | Weight | 52.48 | Kg/m |
|  |  |  |  | % | NF6 Lead | 0.015g/sk |  | Grade | K-55 |  |
|  |  |  |  | % | Econolite Lead | 0.580g/sk |  | Connection | BTC |  |
|  |  | Held pre-tour safety and job meetings |  | % | NF6 Tail | 0.006g/sk |  | Joints | 47 |  |
|  |  |  |  | % | HR-6L Tail | 0.025g/sk |  | Length | 466.14 | m |
| Days since | LTA | 388 |  | Av. Wt Lead/Tail | 12.5p/g /15.6p/g |  | Depth | 472 m from RKB | m |

,66