LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 12 Date: 21-10-2005

Depth: 1100m Progress: 18m Days from Spud: 12

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 244mm at 258m

0600 hrs Update: Run Baker Atlas Logs: Run#2 RCLR

Comments: Drill ahead with 216mm hole to 1100m, circulate, survey, wiper trip, POOH to Log, Run Baker Atlas Logs, Run#1 MLL\DLL\XMAC\ZDL\CN\GR\TIRM.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1082-1100 | Strzelecki Formation - No Show | TG tr-0.5u C1 100% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 4.7 197 2500 | 4.7 227 | +73 -149 | 0 30 Low |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 12

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1082-1100 | STRZELECKI FORMATION Sandstone (50%) with minor thinly interbedded and laminated Claystone (50%). SANDSTONE: light to medium green grey, very fine to fine, dominantly fine, subangular to subrounded, moderately sorted, moderate silica cement, moderate calcareous cement, abundant white argillaceous matrix - matrix supported, abundant altered feldspar and grey green lithic grains, trace orange brown and black lithic grains, trace quartz grains, trace black coaly detritus, hard, no visual porosity, no oil fluorescence. CLAYSTONE: medium grey to medium brown grey to medium green grey, moderately to very silty, often very finely arenaceous with altered lithic grains, trace black carbonaceous flecks, trace black coal detritus, trace micromica, moderately hard, subfissile. |