LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 18 Date: 27-10-2005

Depth: 1268m Progress: 24m Days from Spud: 18

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 178mm at 1097m

0600 hrs Update: Drill ahead with 156mm hole to 1282m, survey. Lithology: Claystone (100%), background gas trace-2 units (C1 100%), cutting samples would indicate the well bore exited the fault plane at around 1273m.

Comments: Survey, POOH for BHA change to reduce hole deviation, RIH, drill ahead 156mm hole with a pendulum drilling assembly (use low WOB and high RPM) trip gas trace. Drill ahead with 156mm hole to 1268m. Samples still have a significant abundance of fracture/vein infill material and slickensiding - suggestive of well path following a fault line. No evidence is present to suggest any open fracture volume.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1244-1268 | Strzelecki Formation - No Show | TG tr-1u C1 100% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 4.7 197 2500 | 4.7 227 | +73 -149 | 0 30 Low |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 18

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1244-1268 | STRZELECKI FORMATION Sandstone (70%) interbedded and laminated with Claystone (30%) and minor Coal (trace). SANDSTONE: light to medium green grey, very fine to medium, dominantly fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, common white argillaceous matrix, abundant altered feldspar and grey green lithic grains, trace orange brown and black lithic grains, trace quartz grains, trace black coaly material, abundant veining infilled by a soft light brown soapy mineral and trace brick red mineral, trace crystalline calcite, hard, no visual porosity, no oil fluorescence. CLAYSTONE: off white to medium grey to medium green grey to medium brown grey, very silty, often very finely arenaceous with altered lithic grains, trace black carbonaceous flecks, common black coal detritus, trace micromica, common slickensided surfaces, common veining infilled by a soft light brown soapy mineral and trace brick red mineral, trace crystalline calcite, moderately hard, subfissile. COAL: black, subvitreous lustre, platy to subconchoidal fracture - slickensided, clean to moderately argillaceous, hard, brittle. |