LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.1 PEP 157

DAILY GEOLOGICAL REPORT No. 1 Date: 10-10-05

Depth: 45m Progress: 45m Days from Spud: 1

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 340mm at 12m

0600 hrs Update: Wait on LCM at 45m.

Comments: Set 13.375" (340mm) conductor at 12m prior to spud. Spud Boundary Creek No.1 at 1900hrs on the 10th of November, 2005 with 12.25" (311mm) hole and gel/starch spud mud, drill ahead to 45m, total loss of returns at 45m in possible coal, mix high viscosity LCM pill.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 12-44 | LaTrobe Formation - No Show. | TG 0u |
| 44-45 | No returns - total loss of circulation. |  |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 4.7 197 2500 | 4.7 | +73 | 0 |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.1 PEP 157

DAILY GEOLOGICAL REPORT No. 1

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 12-44 | LATROBE GROUP Massive Sandstone (100%) SANDSTONE: light orange, very fine to pebble, dominantly very coarse, subangular to rounded, poorly sorted, trace orange brown argillaceous matrix, no visible cement, clear to opaque quartz grains occasionally with yellow brown iron oxide staining, trace black coaly detritus, unconsolidated, very good inferred porosity, no oil fluorescence. |
| 44-45 | No returns - total loss of circulation - probable Coal. |