LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 20 Date: 29-10-2005

Depth: 1416m Progress: 31m Days from Spud: 20

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 178mm at 1097m

0600 hrs Update: Drill ahead with 156mm hole to 1424m, prepare to survey. Current lithology: Claystone (80%) laminated with Sandstone (20%), background gas 1 unit (C1 100%), cutting samples would indicate the well bore is currently exiting the fault plane.

Comments: Drill ahead with 156mm hole to 1397m, survey 8.5 degrees, POOH bit and BHA change to try and control deviation, RIH with strong pendulum drilling assembly, drill ahead with low weight and high RPM to 1416m. Trip gas at 1397m = 1 unit. Well bore appears to have entered a hydrothermally altered fault plane at around 1385m.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1385-1416 | Strzelecki Formation - No Show | TG 0.5-2u C1 100% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 4.7 197 2500 | 4.7 227 | +73 -149 | 0 30 Low |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 20

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1385-1416 | STRZELECKI FORMATION Sandstone (70%) interbedded and laminated with Claystone (30%) and minor Coal (trace). SANDSTONE: light to medium green grey, very fine to medium, dominantly fine, subangular to subrounded, moderately sorted, moderate silica and strong calcareous cements, abundant white argillaceous matrix, abundant altered feldspar, common grey green lithics, trace orange brown and black lithics, trace quartz grains, common black coaly detritus, common to abundant veining infilled by a soft light brown soapy mineral and a bright red mineral, common crystalline calcite, abundant slickensides, hard, no visual porosity, no oil fluorescence. CLAYSTONE: light to medium grey to medium brown grey, very silty, often very finely arenaceous with altered feldspars grains, trace black carbonaceous flecks, common black coal detritus, trace micromica, abundant veining infilled by a soft light brown soapy mineral and a bright red mineral, trace crystalline calcite, abundant slickensides, moderately hard, subfissile. COAL: black to very dark brown grey, earthy to subvitreous lustre, platy to blocky to subconchoidal fracture, clean to dominantly very argillaceous, hard, brittle - the coal has no fluorescence but gives an extremely weak dull light yellow crush cut. |