LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 22 Date: 31-10-2005

Depth: 1548m Progress: 92m Days from Spud: 22

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 178mm at 1097m

0600 hrs Update: Drill ahead with 156mm hole at 1548m. Current lithology Sandstone (30%) interbedded with Claystone (70%), background gas 1-3 units (C1 100%).

Comments: Drill ahead with 156mm hole to 1526m. Trip gas 1 unit. Cutting samples would indicate the well bore re-entered a mineralised fault plane at about 1502m and exited at about 1512m.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1456-1526 | Strzelecki Formation - No Show Maximum gas 4 units (C1 100%) at 1521m. | TG tr-4u C1 100% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 4.7 197 2500 | 4.7 227 | +73 -149 | 0 30 Low |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 22

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1456-1502 | STRZELECKI FORMATION Sandstone (90%) interbedded and laminated with and in part grading to Claystone (10%) and minor detrital Coal (trace). SANDSTONE: light to medium green grey, very fine to medium, dominantly medium, subangular to subrounded, moderately sorted, strong silica and weak calcareous cements, abundant white argillaceous matrix, abundant altered feldspar and grey green lithics, trace orange brown and black lithics, trace quartz grains, trace black coal detritus, hard, very poor visual porosity, no oil fluorescence. CLAYSTONE: light to medium grey to dark brown grey, very silty - grades to siltstone, often very finely arenaceous with altered feldspars grains, trace black carbonaceous flecks, trace black coal detritus, trace micromica, moderately hard, subfissile. COAL: black to very dark brown grey, earthy to subvitreous lustre, platy to subconchoidal fracture, clean to occasionally very argillaceous, hard, brittle - the coal has no fluorescence but gives a weak dull light yellow crush cut. |
| 1502-1512 | STRZELECKI FORMATION Sandstone (100%) and minor Coal (trace) - possible fault zone. SANDSTONE: light to medium green grey, very fine to medium, dominantly fine, subangular to subrounded, moderately sorted, strong silica and weak calcareous cements, abundant white argillaceous matrix, abundant altered feldspar, common grey green lithics, trace orange brown and black lithics, trace quartz grains, common black coaly detritus, abundant veining infilled by a soft light brown soapy mineral and a bright red mineral, common slickensides, hard, no visual porosity, no oil fluorescence. COAL: black to very dark brown grey, earthy to subvitreous lustre, platy to subconchoidal fracture, clean to occasionally very argillaceous, hard, brittle - the coal has no fluorescence but gives a very weak dull light yellow crush cut. |
| 1512-1526 | STRZELECKI FORMATION Sandstone (50%) and interbedded with Claystone (50%) and minor Coal (trace). SANDSTONE: light to medium green grey, very fine to medium, dominantly fine, subangular to subrounded, moderately sorted, strong silica and weak calcareous cements, abundant white argillaceous matrix, abundant altered feldspar, common grey green lithics, trace orange brown and black lithics, trace quartz grains, common black coaly detritus, hard, no visual porosity, no oil fluorescence. CLAYSTONE: light to medium grey to medium brown grey, very silty - grades to siltstone, often very finely arenaceous with altered feldspars grains, trace black carbonaceous flecks, trace black coal detritus, trace micromica, moderately hard, subfissile. COAL: black to very dark brown grey, earthy to subvitreous lustre, platy to subconchoidal fracture, clean to occasionally very argillaceous, hard, brittle - the coal has no fluorescence but gives a very weak dull light yellow crush cut. |