LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 23 Date: 1-11-2005

Depth: 1579m Progress: 31m Days from Spud: 23

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 178mm at 1097m

0600 hrs Update: Drill ahead with 156mm hole at 1598m, trip gas 4 units, current lithology claystone (60%) interbedded and laminated with sandstone (40%), background gas trace-0.5 units.

Comments: Drill ahead with 156mm hole to 1579m, POOH due to high torque, pick up new insert bit, RIH.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1526-1579 | Strzelecki Formation - No Show | TG tr-2u C1 100% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 4.7 197 2500 | 4.7 227 | +73 -149 | 0 30 Low |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 23

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1526-1579 | STRZELECKI FORMATION Sandstone (70%) interbedded and laminated with and in part grading to Claystone (30%). SANDSTONE: light to medium green grey, very fine to occasionally medium, dominantly fine, subangular to subrounded, moderately sorted, strong silica and weak calcareous cements, abundant white argillaceous matrix, abundant altered feldspar, common grey green lithics, trace orange brown and black lithics, trace quartz grains, trace black coaly detritus, hard, nil to very poor visual porosity, no oil fluorescence. CLAYSTONE: light to medium dark grey to medium brown grey, very silty - grades in part to siltstone, often very finely arenaceous with altered feldspars grains - grades to sandstone, trace black carbonaceous flecks, trace micromica, moderately hard, subfissile. |