LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 26 Date: 4-11-2005

Depth: 1849m Progress: 112m Days from Spud: 26

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 178mm at 1097m

0600 hrs Update: Drill ahead with 156mm hole at 1871m. Current lithology: Sandstone (80%) laminated with claystone (20%) and trace coal, background gas 1 unit.

Comments: Drill ahead with 156mm hole to 1835m, wiper trip, drill ahead with 156mm hole to 1849m.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1737-1849 | Strzelecki Formation - No Show Maximum gas of 4 units at 1849m from coal. | TG tr-4u C1 100% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 4.7 197 2500 | 4.7 227 | +73 -149 | 0 30 Low |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 26

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1737-1849 | STRZELECKI FORMATION Sandstone (80%) interbedded and laminated with and in part grading to Claystone (20%) with minor Coal (trace). SANDSTONE: light to medium green grey, very fine to medium, dominantly fine, subangular to subrounded, moderately sorted, strong silica and weak to moderate calcareous cements, abundant white argillaceous matrix - matrix supported, abundant altered feldspar, common grey green lithics, trace orange brown and black lithics, trace quartz grains, trace to common black coal detritus, hard, nil to very poor visual porosity, no oil fluorescence. CLAYSTONE: off white to medium dark grey to medium brown grey, very silty in part, often very finely arenaceous with altered feldspars grains, slightly calcareous where arenaceous, trace black carbonaceous flecks, trace black coal detritus, trace micromica, moderately hard, subfissile. COAL: black to dark brown grey, earthy where argillaceous, subvitreous where clean, platy to subconchoidal fracture, very argillaceous in part, hard, brittle. CUT: The coal has no fluorescence but gives a weak dull pale yellow crush cut. |