LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 32 Date: 10-11-2005

Depth: 2135m Progress: 94m Days from Spud: 32

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 178mm at 1097m

0600 hrs Update: Drill ahead with 156mm hole at 2154m. Current lithology: Claystone (90%) with laminated Sandstone (10%), background gas 0.5 units (C1 100%), no peaks.

Comments: Drill ahead with 156mm hole to 2135m. Samples taken at 2070m and 2072m (gladwrap/alfoil/wax sealed) for source rock/gas composition analysis (best sample 2072m). Desorption gas analysis from cuttings sample at 2071m on rig chromatograph gave trace C1 gas only - note: chromatograph calibration range and sensitivity at rig site is unsuitable for detailed analysis.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 2041-2135 | Strzelecki Formation - No Show Maximum gas at 2071m from coal. | TG tr-3.5u C1 100% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 4.7 197 2500 | 4.7 227 | +73 -149 | 0 30 Low |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 32

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 2041-2071 | STRZELECKI FORMATION Claystone (70%) with laminated Sandstone (30%) with minor Coal (trace). CLAYSTONE: light to medium dark grey to medium brown grey, dominantly medium dark grey, very silty in part, very finely arenaceous with altered feldspars grains in part, slightly calcareous where arenaceous, trace black carbonaceous flecks, trace black coal detritus, common micromica, moderately hard, subfissile. SANDSTONE: light to medium green grey, silty to fine, dominantly very fine, subangular to subrounded, moderately sorted, strong silica and weak calcareous cements, abundant white argillaceous matrix - matrix supported, abundant altered feldspar, common grey green lithics, rare orange brown and black lithics, trace quartz grains, trace black coal detritus, hard, no visual porosity, no oil fluorescence. COAL: black to dark brown grey, dominantly very argillaceous - occasionally clean, earthy with irregular to platy fracture where argillaceous, subvitreous with subconchoidal fracture where clean, hard, brittle. CUT: The coal has no fluorescence but gives a weak dull pale yellow crush cut. |
| 2071-2135 | STRZELECKI FORMATION Sandstone (80%) interbedded and laminated with Claystone (20%) and minor Coal (trace). SANDSTONE: light to medium green grey, very fine to medium, dominantly fine, subangular to subrounded, moderately sorted, strong silica and weak calcareous cements, abundant white argillaceous matrix - matrix supported, abundant altered feldspar, common grey green lithics, rare orange brown and black lithics, trace quartz grains, trace black coal detritus, hard, no visual porosity, no oil fluorescence. CLAYSTONE: light to medium dark grey to medium brown grey, dominantly medium grey, very silty in part, very finely arenaceous with altered feldspars grains in part, slightly calcareous where arenaceous, trace black carbonaceous flecks, trace black coal detritus, common micromica, moderately hard, subfissile. COAL: black to dark brown grey, dominantly very argillaceous - occasionally clean, earthy with irregular to platy fracture where argillaceous, subvitreous with subconchoidal fracture where clean, hard, brittle.The coal has no fluorescence but gives a weak dull pale yellow crush cut. |