LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 33 Date: 11-11-2005

Depth: 2161m Progress: 26m Days from Spud: 33

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 178mm at 1097m

0600 hrs Update: Drill ahead with 156mm hole at 2177m. Lithology 2161-2173 Claystone (80%) laminated with 20% very fine sandstone, 2173-2177m fine sandstone (50%) laminated with claystone (50%). Background gas 0.5 units, no peaks.

Comments: Drill ahead with 156mm hole to 2158m, survey, POOH for new bit. (Survey at 2146m = 6.4°, BHT 61.3° C). RIH with new bit, drill ahead with 156mm hole to 2161m. Trip gas trace.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 2135-2161 | Strzelecki Formation - No Show | TG tr-1u C1 100% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 4.7 197 2500 | 4.7 227 | +73 -149 | 0 30 Low |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 33

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 2135-2161 | STRZELECKI FORMATION Sandstone (70%) interbedded and laminated with Claystone (30%). SANDSTONE: light to medium green grey, very fine to medium, dominantly fine, subangular to subrounded, moderately sorted, strong silica and weak calcareous cements, abundant white argillaceous matrix - matrix supported, abundant altered feldspar, common grey green lithics, rare orange brown and black lithics, trace quartz grains, trace black coal detritus, trace quartz vein infill in part, hard, no visual porosity, no oil fluorescence. CLAYSTONE: off white to medium dark grey to medium brown grey, very silty in part, very finely arenaceous with altered feldspars grains in part, slightly calcareous where arenaceous, slightly carbonaceous in part, trace black coal flecks and detritus, common micromica, trace quartz vein infill in part, moderately hard, subfissile. |