LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 34 Date: 12-11-2005

Depth: 2193m Progress: 32m Days from Spud: 34

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 178mm at 1097m

0600 hrs Update: RIH with new 6" (152mm) bit, drill ahead with 152mm hole at 2206m. Trip gas trace. Current lithology claystone (80%) with laminated fine sandstone (20%), background gas 0.5 units.

Comments: Drill ahead with 156mm hole to 2193m, POOH due to low ROP, RIH with new 152mm (6") bit.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 2161-2193 | Strzelecki Formation - No Show | TG tr-1u C1 100% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 4.7 197 2500 | 4.7 227 | +73 -149 | 0 30 Low |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 34

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 2161-2193 | STRZELECKI FORMATION Sandstone (40%) interbedded and laminated with Claystone (60%). SANDSTONE: light to medium green grey, very fine to fine, dominantly fine, subangular to subrounded, moderately sorted, strong silica and weak calcareous cements, abundant white argillaceous matrix - matrix supported, abundant altered feldspar grains, common grey green lithics, rare orange brown and black lithics, trace quartz grains, trace black coal detritus, hard, no visual porosity, no oil fluorescence. CLAYSTONE: off white to medium dark grey to medium brown grey, often very silty - grades to siltstone, very finely arenaceous with altered feldspars grains in part, slightly calcareous where arenaceous, slightly carbonaceous in part, trace black coal flecks and detritus, common micromica, hard, subfissile. |