LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 42 Date: 20-11-2005

Depth: 2341m Progress: 0m Days from Spud: 41

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 178mm at 1097m

0600 hrs Update: Continue Mechanical sidewall coring.

Comments: Continue running Electric Logs: Run #4 Memorex-GR (tool malfunction part way through run - irreparable), POOH with memorex, RIH for Run #5 (continuation of VSP), tool malfunction, POOH with velocity tool for repairs, RIH, complete VSP, RIH for Run#6 mechanical sidewall cores, cut 4, POOH to check tool, recovered 4, RIH to continue SWC's.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
|  | No new formation drilled. |  |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 3.7 197 2500 | 3.7 227 2341 | +74 -149 -2263 | 0 30 Low 159 High |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 42

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
|  | No new formation drilled. |