LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 4 Date: 13-10-2005

Depth: 132m Progress: 61m Days from Spud: 4

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 340mm at 69m

0600 hrs Update: Drill ahead with 311mm hole at 220m in LaTrobe Group sandstone.

Comments: Pull conductor, open hole out to 17.5" (444mm), POOH, run 13.375" (340mm) casing to 69m, RIH with 12.25" (311mm) drilling assembly, drill ahead to 132m.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 71-132 | LaTrobe Group - No Show | TG 0u |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 4.7 197 2500 | 4.7 | +73 | 0 |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 4

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 71-132 | LATROBE GROUP Massive Sandstone (100%). SANDSTONE: very light grey, fine to pebble, dominantly very coarse, angular to subrounded, very poorly sorted, no visible matrix, no visible cement, opaque to milky quartz grains, trace grey cherty lithics, trace black coaly detritus, unconsolidated, very good inferred porosity, no oil fluorescence. |