LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 5 Date: 14-10-2005

Depth: 261m Progress: 129m Days from Spud: 5

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 244mm at 258m

0600 hrs Update: WOC, nipple up BOP's.

Comments: Drill ahead with 311mm hole to 261m, condition hole, POOH to run 9.625" (244mm) casing to 258m, WOC.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 132-227 | LaTrobe Group - No Show | TG 0u |
| 227-261 | Strzelecki Formation - No Show | TG 0-1u C1 100% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 4.7 197 2500 | 4.7 227 | +73 -149 | 0 30 Low |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 5

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 132-219 | LATROBE GROUP Sandstone (95%) with minor interbedded Claystone (5%). SANDSTONE: very light grey, fine to pebble, dominantly very coarse to granular, angular to subrounded, very poorly sorted, no visible matrix, no visible cement, opaque to milky quartz grains, trace grey cherty lithics, trace black coaly detritus, unconsolidated, very good inferred porosity, no oil fluorescence. CLAYSTONE: light grey to medium brown, trace black coal detritus, trace pyrite, very soft, very dispersive, non fissile. |
| 219-227 | LATROBE GROUP (Reworked Strzelecki?) Massive Sandstone (100%). SANDSTONE: light grey, with fine to pebble angular to subrounded very poorly sorted opaque to milky quartz grains intermixed with abundant off white altered feldspar grains and common altered grey green and brown lithic grains, trace black coal detritus, unconsolidated, good inferred porosity, no oil fluorescence. |
| 227-261 | STRZELECKI FORMATION Sandstone (70%) thinly interbedded and laminated with Claystone (30%). SANDSTONE: light to medium grey to medium green grey, very fine to coarse, dominantly medium to coarse, subangular to subrounded, moderately sorted, weak silica cement, common to abundant white argillaceous matrix, abundant altered feldspar and grey green and brown lithic grains, common quartz grains, trace black carbonaceous material, friable, poor to fair visual porosity, no oil fluorescnce. CLAYSTONE: light grey to medium green grey to medium brown grey, moderately silty, trace black carbonaceous flecks, trace pyrite, soft, very dispersive, non fissile. |