LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 8 Date: 17-10-2005

Depth: 743m Progress: 234m Days from Spud: 8

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 244mm at 258m

0600 hrs Update: Drill ahead with 216mm hole at 788m. Lithology: Interbedded Sandstone (40%) with Claystone (60%), background gas trace-1 unit, C1 100%.

Comments: Drill ahead with 216mm hole to 600m, survey = 1.5 degrees, wiper trip, drill ahead to 743m. Possible fracture/fault zone 630-636m, no associated gas increase or oil fluorescence.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 509-636 | Strzelecki Formation - No Show | TG tr-0.5u C1 100% |
| 636-723 | Strzelecki Formation - No Show | TG tr-1u C1 100% |
| 723-743 | Strzelecki Formation - No Show | TG tr-1u C1 100% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 4.7 197 2500 | 4.7 227 | +73 -149 | 0 30 Low |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 8

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 509-636 | STRZELECKI FORMATION Sandstone (50%) interbedded and laminated with Claystone (50%). SANDSTONE: light to medium green grey, very fine to coarse, rarely very coarse, dominantly medium, subangular to subrounded, moderately sorted, weak silica cement, weak calcareous cement where coarse, common to abundant white argillaceous matrix, abundant altered feldspar and grey green lithic grains, trace brown and black lithic grains, trace quartz grains, trace coarse brown mica flakes and common quartz grains where coarse, trace to occasionally common black coaly detritus, trace pyrite, occasionally common calcite vein infill, friable to moderately hard, very poor to fair visual porosity - fair visual porosity where coarse, no oil fluorescnce. CLAYSTONE: medium grey to medium brown grey to medium green grey, very silty, very finely arenaceous with altered lithic grains in part, slightly carbonaceous in part, trace black coaly flecks, trace to occasionally common black coal detritus, trace pyrite, occasionally common calcite vein infill, soft, non fissile. |
| 636-723 | STRZELECKI FORMATION Sandstone (50%) interbedded and laminated with Claystone (50%). SANDSTONE: light to medium green grey, very fine to medium, dominantly fine, subangular to subrounded, moderately sorted, weak silica cement, weak to moderate calcareous cement, abundant white argillaceous matrix - matrix supported in part, abundant altered feldspar and grey green lithic grains, trace brown and black lithic grains, trace to common quartz grains, trace black coal detritus, trace calcite vein infill in part, friable to moderately hard, very poor to poor visual porosity, no oil fluorescnce. CLAYSTONE: medium grey to medium brown grey to medium green grey, very silty, very finely arenaceous with altered lithic grains in part, trace black coaly flecks, trace black coal detritus, trace pyrite, trace calcite vein infill, soft, non fissile. |
| 723-743 | STRZELECKI FORMATION Sandstone (100%) interbedded and laminated with Claystone (trace). SANDSTONE: medium green grey, very fine to coarse, dominantly medium to coarse, subangular to subrounded, moderately sorted, weak silica and calcareous cements, common white argillaceous matrix, abundant altered feldspar and grey green lithic grains, common red brown and black lithic grains, common quartz grains, trace coarse brown mica flakes, trace black coal detritus, friable, fair visual porosity, no oil fluorescnce. CLAYSTONE: off white to medium grey to medium brown grey to medium green grey, moderately silty, occasionally very finely arenaceous with altered lithic grains, trace black carbonaceous flecks and detritus, trace micromica, soft, non fissile. |