LAKES OIL N.L. CUTTINGS DESCRIPTIONS WELL NAME: BOUNDARY CREEK No.2 DATE: 18-10-2005 GEOLOGIST: David Horner PAGE: 1

| Interval (m) | % | Description |
| --- | --- | --- |
| 777-789 | 90 | SANDSTONE: light to medium green grey, very fine to coarse, dominantly medium, subangular to subrounded, moderately sorted, moderate silica and weak calcareous cements, abundant white argillaceous matrix, abundant altered feldspar and grey green lithic grains, trace orange brown and black lithic grains, trace to common quartz grains, trace coarse brown mica flakes, trace black carbonaceous material, hard, very poor visual porosity, no oil fluorescnce. |
|  | 10 | CLAYSTONE: off white to medium grey to medium green grey to medium brown grey, moderately to very silty, occasionally very finely arenaceous with altered lithic grains, trace black carbonaceous flecks and detritus, trace micromica, soft, non fissile. |
| 789-798 | 100 | SANDSTONE: as for 777-789m. |
| 798-807 | 100 | SANDSTONE: light to medium green grey, very fine to coarse, dominantly medium to coarse, subangular to subrounded, moderately sorted, moderate silica and weak calcareous cements, abundant white argillaceous matrix, abundant altered feldspar and grey green lithic grains, trace orange brown and black lithic grains, common quartz grains, trace coarse brown mica flakes, trace to common black carbonaceous material, hard, very poor visual porosity, no oil fluorescnce. |
| 807-810 | 90 | SANDSTONE: as for 798-807m. |
|  | 10 | CLAYSTONE: off white to medium brown grey to medium green grey, moderately to very silty, occasionally very finely arenaceous with altered lithic grains, trace black carbonaceous flecks and detritus, trace micromica, soft, non fissile. |
| 810-819 | 90 | SANDSTONE: light to medium green grey, very fine to coarse, dominantly medium, subangular to subrounded, moderately sorted, moderate silica and weak calcareous cements, abundant white argillaceous matrix, abundant altered feldspar and grey green lithic grains, trace orange brown and black lithic grains, common quartz grains, trace coarse brown mica flakes, trace to common black carbonaceous material, hard, very poor visual porosity, no oil fluorescnce. |
|  | 10 | CLAYSTONE: as for 807-810m. |
| 819-828 | 100 | SANDSTONE: as for 810-819m. |
| 828-831 | 90 | SANDSTONE: as for 810-819m. |
|  | 10 | CLAYSTONE: off white to medium brown grey to medium green grey, very silty, occasionally very finely arenaceous with altered lithic grains, trace black carbonaceous flecks and detritus, trace micromica, soft, non fissile. |
| 831-837 | 100 | SANDSTONE: medium green grey, very fine to coarse, dominantly medium, subangular to subrounded, moderately sorted, moderate silica and weak calcareous cements, abundant white argillaceous matrix, abundant altered feldspar and grey green lithic grains, trace orange brown and black lithic grains, common quartz grains, trace coarse brown mica flakes, trace black carbonaceous material, hard, very poor visual porosity, no oil fluorescnce. |
| 837-840 | 80 | SANDSTONE: as for 831-837m. |
|  | 20 | CLAYSTONE: off white to medium brown grey to medium green grey, very silty, occasionally very finely arenaceous with altered lithic grains, trace black carbonaceous flecks and detritus, trace micromica, firm, non to slightly subfissile. |
| 840-846 | 100 | SANDSTONE: light to medium green grey, very fine to coarse, dominantly medium, subangular to subrounded, moderately sorted, moderate silica and weak calcareous cements, abundant white argillaceous matrix, abundant altered feldspar and grey green lithic grains, trace orange brown and black lithic grains, common quartz grains, trace coarse brown mica flakes, trace black carbonaceous material, hard, very poor visual porosity, no oil fluorescnce. |
| 846-855 | 100 | SANDSTONE: light to medium green grey, very fine to coarse, dominantly medium, subangular to subrounded, moderately sorted, moderate silica and weak calcareous cements, abundant white argillaceous matrix, abundant altered feldspar and grey green lithic grains, trace orange brown and black lithic grains, common quartz grains, trace coarse brown mica flakes, common black coaly detritus, hard, very poor to poor visual porosity, no oil fluorescnce. |
| 855-864 | 100 | SANDSTONE: light to medium green grey, very fine to coarse, dominantly medium, subangular to subrounded, moderately sorted, moderate silica and weak calcareous cements, common white argillaceous matrix, abundant altered feldspar and grey green lithic grains, trace orange brown and black lithic grains, common quartz grains, trace coarse brown mica flakes, common black coaly detritus, hard, very poor to poor visual porosity, no oil fluorescnce. |
| 864-867 | 70 | SANDSTONE: light to medium green grey, very fine to occasionally coarse, dominantly fine to medium, subangular to subrounded, moderately sorted, moderate silica and calcareous cements, abundant white argillaceous matrix, abundant altered feldspar and grey green lithic grains, trace orange brown and black lithic grains, trace quartz grains, trace coarse brown mica flakes, trace black coaly detritus, hard, very poor visual porosity, no oil fluorescnce. |
|  | 30 | CLAYSTONE: medium to dark brown grey to medium grey, very silty, occasionally very finely arenaceous with altered lithic grains, trace black carbonaceous flecks and detritus, trace micromica, firm, slightly subfissile. |
| 867-870 | 90 | SANDSTONE: as for 864-867m. |
|  | 10 | CLAYSTONE: as for 864-867m. |
| 870-876 | 100 | SANDSTONE: light to medium green grey, very fine to coarse, dominantly medium, subangular to subrounded, moderately sorted, moderate silica and weak calcareous cements, common to abundant white argillaceous matrix, abundant altered feldspar and grey green lithic grains, trace orange brown and black lithic grains, common quartz grains, trace coarse brown mica flakes, trace black coaly detritus, hard, very poor to poor visual porosity, no oil fluorescnce. |
| 876-882 | 80 | SANDSTONE: as for 870-876m. |
|  | 20 | CLAYSTONE: medium grey to medium brown grey to medium brown, very silty, occasionally very finely arenaceous with altered lithic grains, trace black carbonaceous flecks and detritus, trace micromica, firm, slightly subfissile. |
| 882-885 | 60 | SANDSTONE: light to medium green grey, very fine to occasionally coarse, dominantly fine to medium, subangular to subrounded, moderately sorted, moderate silica and calcareous cements, abundant white argillaceous matrix, abundant altered feldspar and grey green lithic grains, trace orange brown and black lithic grains, trace quartz grains, trace coarse brown mica flakes, trace black coaly detritus, hard, very poor visual porosity, no oil fluorescnce. |
|  | 40 | CLAYSTONE: as for 876-882m. |
| 885-888 | 70 | SANDSTONE: as for 882-885m. |
|  | 30 | CLAYSTONE: medium grey to medium brown grey to medium brown to medium green grey, very silty, occasionally very finely arenaceous with altered lithic grains, trace black carbonaceous flecks and detritus, trace micromica, firm, slightly subfissile. |
| 888-891 | 40 | SANDSTONE: light to medium green grey, very fine to occasionally coarse, dominantly fine to medium, subangular to subrounded, moderately sorted, moderate silica and calcareous cements, abundant white argillaceous matrix, abundant altered feldspar and grey green lithic grains, trace orange brown and black lithic grains, trace quartz grains, common to abundant black coaly detritus, hard, very poor visual porosity, no oil fluorescnce. |
|  | 60 | CLAYSTONE: medium grey to medium brown grey to medium brown to medium green grey, very silty, occasionally very finely arenaceous with altered lithic grains, trace black carbonaceous flecks, common to abundant black coal detritus, trace micromica, firm, slightly subfissile. |
| 891-897 | 70 | SANDSTONE: light to medium green grey, very fine to coarse, dominantly medium, subangular to subrounded, moderately sorted, moderate silica and weak calcareous cements, common to abundant white argillaceous matrix, abundant altered feldspar and grey green lithic grains, trace orange brown and black lithic grains, common quartz grains, common black coaly detritus, hard, very poor to poor visual porosity, no oil fluorescnce. |
|  | 30 | CLAYSTONE: medium grey to medium brown grey to medium brown to medium green grey, very silty, occasionally very finely arenaceous with altered lithic grains, trace black carbonaceous flecks, common black coal detritus, trace micromica, firm, slightly subfissile. |
| 897-900 | 90 | SANDSTONE: light to medium green grey, very fine to coarse, dominantly medium, subangular to subrounded, moderately sorted, moderate silica and weak calcareous cements, common to abundant white argillaceous matrix, abundant altered feldspar and grey green lithic grains, trace orange brown and black lithic grains, common quartz grains, trace coarse brown mica flakes, trace black coaly detritus, hard, very poor to poor visual porosity, no oil fluorescnce. |
|  | 10 | CLAYSTONE: medium grey to medium brown grey to medium brown to medium green grey, very silty, occasionally very finely arenaceous with altered lithic grains, trace black carbonaceous flecks, trace black coal detritus, trace micromica, firm, slightly subfissile. |
| 900-903 | 100 | SANDSTONE: light to medium green grey, very fine to coarse, dominantly medium, subangular to subrounded, moderately sorted, moderate silica and weak calcareous cements, common to abundant white argillaceous matrix, abundant altered feldspar and grey green lithic grains, trace orange brown and black lithic grains, common quartz grains, trace coarse brown mica flakes, common black coaly detritus, hard, very poor to poor visual porosity, no oil fluorescnce. |
| 903-906 | 90 | SANDSTONE: light to medium green grey, very fine to coarse, dominantly medium, subangular to subrounded, moderately sorted, moderate silica and weak calcareous cements, common to abundant white argillaceous matrix, abundant altered feldspar and grey green lithic grains, trace orange brown and black lithic grains, common quartz grains, trace coarse brown mica flakes, trace black coaly detritus, hard, very poor to poor visual porosity, no oil fluorescnce. |
|  | 10 | CLAYSTONE: medium grey to medium brown grey to medium green grey, very silty, occasionally very finely arenaceous with altered lithic grains, trace black carbonaceous flecks, trace black coal detritus, trace micromica, firm, slightly subfissile. |