LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 9 Date: 18-10-2005

Depth: 884m Progress: 141m Days from Spud: 9

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 244mm at 258m

0600 hrs Update: Drill ahead with 216mm hole at 911m. Lithology: Sandstone (80%) thinly interbedded and laminated with Claystone (20%), gas 0.5-2 units (C1 100%).

Comments: Drill ahead with 216mm hole to 797m, survey = 2.0 degrees, wiper trip (wiper trip gas = trace), drill ahead with 216mm hole to 884m.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 743-775 | Strzelecki Formation - No Show | TG tr-0.6u C1 100% |
| 775-884 | Strzelecki Formation - No Show | TG tr-1u C1 100% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 4.7 197 2500 | 4.7 227 | +73 -149 | 0 30 Low |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 9

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 743-775 | STRZELECKI FORMATION Claystone (80%) interbedded and laminated with Sandstone (20%). SANDSTONE: light to medium green grey, very fine to medium, dominantly fine, subangular to subrounded, moderately sorted, weak silica and moderate calcareous cements, abundant white argillaceous matrix, abundant altered feldspar and grey green lithic grains, trace orange brown and black lithic grains, trace quartz grains, trace black carbonaceous material, moderately hard, very poor visual porosity, no oil fluorescnce. CLAYSTONE: off white to medium grey to medium green grey to medium brown grey, moderately silty, occasionally very finely arenaceous with altered lithic grains, trace black carbonaceous flecks and detritus, trace micromica, soft, non fissile. |
| 775-884 | STRZELECKI FORMATION Sandstone (90%) with minor thinly interbedded and laminated Claystone (10%). SANDSTONE: light to medium green grey, very fine to coarse, dominantly medium, subangular to subrounded, moderately sorted, moderate silica and weak calcareous cements, common to abundant white argillaceous matrix, abundant altered feldspar and grey green lithic grains, trace orange brown and black lithic grains, common quartz grains, trace coarse brown mica flakes, common black coaly detritus, hard, very poor to poor visual porosity, no oil fluorescnce. CLAYSTONE: off white to medium brown grey to medium green grey, very silty, occasionally very finely arenaceous with altered lithic grains, trace black carbonaceous flecks and detritus, trace micromica, firm, non to slightly subfissile. |