LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Boundary creek-2 | REPORT No. : | 20 | DFS: | 19 | DATE : | 29 Oct-05 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 1416m | LAST DEPTH : | 1385m | 24 HR PROGRESS : | 31m | PTD : | 2500m |
| TOTAL FUEL : | 9,550 | FUEL USAGE : | 2,650 |  | 29,958 | CUM. COST : $ | 1,257,797 |
| 0600 OPS : | Drilling 156mm hole at 1424m Ran survey at 1424m 8.5deg |
| Next 24 hr OPS: | Drill ahead |
| Site Personnel: | Lakes 3 A.M.C 1- Mud logger 2- Hunt Energy 19 |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 6 | 7 Re-Run |  | Drilling | 15.00 |  | Density | 9.30 | ppg |
| Size (mm) | 156 | 156 |  | Tripping | 7.00 |  | Viscosity | 41 | Sec |
| Make | Reed | Varel |  | Surveys | 1.00 |  | PV @ Deg C | 14 | Deg C |
| Type | SL43HP | M-332 |  | Reaming |  |  | YP lbs/100 ft 2 | 11 | Lbs/100ft |
| IADC Code | 4-3-7 |  |  | Slip and cut block line |  |  | API Filtrate | 7.4 | m/30min |
| Serial Number | JK 4699 | MSK56G1 |  | Circulate and clean hole | 1.00 |  | Gels lbs/100 ft 2 | 2 / 3 / 5 |  |
| Nozzles (32) | 13-14-16 | 14-14-14 |  | Cement casing |  |  | Cake 32nds/ in | 1 |  |
| Depth in (m) | 1100 | 1244 |  | Rig repair |  |  | Sand | 0.20 | % Vol |
| Depth out (m) | 1244 |  |  | Off payroll |  |  | Solids | 7.1 | % Vol |
| Total Metres | 144 | 172 |  | Run Casing |  |  | Hardness Ca mg/l | 70 |  |
| Hours | 34 | 46 |  | Rig Service |  |  | KCL Concentration | 1.42 | % by wt |
| WOB (kg) | 7000 | 5000 |  | Test BOP |  |  | Chlorides | 9,000 | Mg/l |
| RPM | 100 | 120 |  | Drill out Cmt |  |  | Methyl Blue | 9.2 | Ppb equiv |
| Condition |  |  |  | Logging |  |  | K+ | 7,500 | Mg/l |
| Impact Force | 166lb/ft |  |  | W.0.C |  |  | Daily Cost $ | 1,381 |
| Jet Velocity | 150ft/sec |  |  | Install BOP |  |  | Cum Cost $ | 33,145 |
| B.H.A.: | Bit- Bit sub 3 x 4-3/4inch drill collars- stabilizer -10 x 4-3/4inch drill collars-Jars-2 x 4-3/4 inch drill collars -4 x Hevi-Wate drillpipe |
|  | BHA length Weight below Jars |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 7.00 | ° at | 1282m | m |  | Type | Amount |
| 00:00 |  | Drilled 156mm hole from 1385m to 13962m with |  | 8.00 | ° at | 1346m | m |  | Defoamer | 1 |
|  | 05:30 | controlled drilling rate to drop deviation angle |  | 8.00 | ° at | 1387m | m |  | AMC Pac-R | 4 |
| 05:30 | 06:00 | Circulated |  | 3.00 | ° at | 1096m | m |  | Caustic | 1 |
| 06:00 | 06:30 | Ran survey at 1387m |  | 4.25 | ° at | 1147m | m |  | Starlose / Barite | 4 / 15 |
| 06:30 | 07:00 | Pumped pill |  | 5.00 | ° at | 1195m | m |  | Potassium chloride | 10 |
| 07:00 | 10:00 | Tripped out for bit change and BHA change |  | 6.00 | ° at | 1214m | m |  | Soium Bicarbonate | 1 |
| 10:00 | 1300 | Tripped in hole to 1117m |  | 6.50 | ° at | 1243m | m |  | Sodium sulphite | 1 |
| 13:00 | 13:30 | Filled pipe with mud |  |  |  |  |
| 13:30 | 14:00 | Tripped in hole to 1385m |  | PUMP 1 |  | PUMP 2 |
| 14:00 | 14:30 | Washed and cleaned hole to bottom at 1396m |  | Liner | 140 | mm |  | Liner | 140 | mm |
| 14;30 |  | Drilled 156mm hole from 1396m to 1416m with |  | Pressure | 8,000 | kPa |  | Pressure |  | KPa |
|  | 24:00 | controlled drilling rate for deviation drop |  | A.V. DP | 221 | ft/min |  | A.V. DP |  | m/min |
|  |  |  |  | A.V. DC | 323 | ft/min |  | A.V. DC |  | m/min |
|  |  |  |  | SPM | 46 |  | SPM |  |
|  |  |  |  | GPM | 228 |  | GPM |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  | Control drilling wt on bit to drop angle on bottom |  | Sacks |  |  | Size | 178mm |  |
|  |  |  |  | Class |  |  | Weight | 38.69 | Kg/m |
|  |  |  |  |  |  |  |  | Grade | N-80 |  |
|  |  |  |  |  |  |  |  | Connection | Buttress |  |
|  | JSA | Working at heights |  |  |  |  |  | Joints | 92 |  |
|  |  | Stabbing drill pipe |  |  |  |  |  | Length |  | m |
| Days since | LTA | 360 |  |  |  |  | Shoe | 1097 | m |

,66