LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Boundary creek-2 | REPORT No. : | 25 | DFS: | 24 | DATE : | 3-Nov-05 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 1737m | LAST DEPTH : | 1643m | 24 HR PROGRESS : | 94m | PTD : | 2500m |
| TOTAL FUEL : |  | FUEL USAGE : |  |  | 35,435 | CUM. COST : $ | 1,414,207 |
| 0600 OPS : | Drilling 156mm hole at |
| Next 24 hr OPS: | Drill ahead with 156mm Bit |
| Site Personnel: | Lakes 3- A.M.C 1- Mud logger 2- Hunt Energy 19 |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | Run 11 Bit # 8 | Run # 12 Bit # 9 |  | Drilling | 17.00 |  | Density | 9.30 | ppg |
| Size (mm) | 156mm | 156mm |  | Tripping | 6.00 |  | Viscosity | 39 | Sec |
| Make | Reed | Reed |  | Surveys |  |  | PV @ Deg C | 14 | Deg C |
| Type | SL43HP | SL51HP |  | Reaming |  |  | YP lbs/100 ft 2 | 7 | Lbs/100ft |
| IADC Code | 4-3-7 | 5-3-7 |  | Slip and cut block line |  |  | API Filtrate | 6.2 | m/30min |
| Serial Number | JK4700 | HP998 |  | Circulate and clean hole | 0.50 |  | Gels lbs/100 ft 2 | 1 / 2 / 2 |  |
| Nozzles (32) | 13-16-16 | 16-16-13 |  | Cement casing |  |  | Cake 32nds/ in | 1 |  |
| Depth in (m) | 1581 | 1643 |  | Rig repair |  |  | Sand | 0.25 | % Vol |
| Depth out (m) | 1643 |  |  | Surveys |  |  | Solids | 6.4 | % Vol |
| Total Metres | 62 | 94 |  | Run Casing |  |  | Hardness Ca mg/l | 180 |  |
| Hours | 21.50 | 17 |  | Rig Service | 0.50 |  | KCL Concentration | 1.50 | % by wt |
| WOB (kg) | 8000 | 8000 |  | Test BOP |  |  | Chlorides | 8,600 | Mg/l |
| RPM | 100 | 100 |  | Drill out Cmt |  |  | Methyl Blue | 8.0 | Ppb equiv |
| Condition | 2-2-NO-A-E-I-NO-PR | In hole |  | Logging |  |  | K+ | 8,000 | Mg/l |
| Impact Force | 162ft/lb | 116lb/ft |  | W.0.C |  |  | Daily Cost $ | 1,608 |
| Jet Velocity | 155ft/sec | 122ft/sec |  | Cement plug |  |  | Cum Cost $ | 41,703 |
| B.H.A.: | Bit- Bit sub- 2 x 4-3/4inch drill collars- stabilizer -11 x 4-3/4 inch drill collars – Jars-2 x 4-3/4 inch drill collars-4 x Hevi-Wate drillpipe |
|  | BHA Length 185.75m Weight below Jars 22,000lbs |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 7.00 | ° at | 1282 | m |  | Type | Amount |
| 00:00 | 01:30 | Tripped out from 567m to surface |  | 8.00 | ° at | 1346 | m |  | Baradefoam | 1 |
| 01:30 | 04:30 | Changed Bit then tripped in hole to 1089m |  | 8.00 | ° at | 1387 | m |  | Sodium sulphite | 1 |
| 04:30 | 05:00 | Filled pipe with mud |  | 8.50 | ° at | 1415 | m |  | AMC PAC-R / L | 3 / 7 |
| 05:00 | 06:30 | Tripped in hole from 1089m to 1643m |  | 8.50 | ° at | 1452 | m |  | Sodium Bicarb | 1 |
| 06:30 | 20:00 | Drilled 156mm hole from 1643m to 1720m |  | 9.00 | ° at | 1489 | m |  | Potassium chloride | 2 |
| 20:00 | 20:30 | Serviced the rig |  | 9.50 | ° at | 1575 | m |  | Pac-L Antisol | 1 |
| 20:30 | 24:00 | Drilled 156mm hole from 1720m to 1737m |  |  | ° at |  | m |  | Caustic | 1 |
|  |  |  |  | PUMP 1 |  | PUMP 2 |
|  |  |  |  | Liner | 140 | mm |  | Liner | 140 | mm |
|  |  |  |  | Pressure | 8,000 | kPa |  | Pressure |  | KPa |
|  |  |  |  | A.V. DP | 192 | ft/min |  | A.V. DP |  | m/min |
|  |  |  |  | A.V. DC | 281 | ft/min |  | A.V. DC |  | m/min |
|  |  |  |  | SPM | 40 |  | SPM |  |
|  |  |  |  | GPM | 200 |  | GPM |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks |  |  | Size | 244mm |  |
|  |  |  |  | Class |  |  | Weight | 53.57 | Kg/m |
|  |  |  |  |  |  |  |  | Grade | K-55 |  |
|  |  |  |  |  |  |  |  | Connection | Buttress |  |
|  | JSA | Changing ou elevators |  |  |  |  |  | Joints | 21 |  |
|  |  | Kick drill |  |  |  |  |  | Length | 253 | m |
| Days since | LTA | 365 |  |  |  |  | Shoe | 258 | m |

,66