LAKES OIL N.L.

DAILY DRILLING REPORT

| WELL: Boundary Creek-2 | REPORT No.: 27 | DATE: 05NOV 05 |
| --- | --- | --- |
| DFS: 26 | 2400 DEPTH: 1898 | Last Depth: 1849 |
| 24hr Progress: 49m | PTD: 2500 | Total Fuel: 8,800 |
| Fuel Usage: 2450 | Daily Cost: 26,827 | Cum Cost: 1,468,944 |
| 0600hrs Operation: Prepare to set Cement plug from 220m to 180m inside the 178mmCasing |
| Next 24hr Operation: Set plug-Cement annulus from surface to 121m ( Hole in Casing depth ) |
| Site Personnel: Lakes 3-AMC 1-Higgins 2-Hunt 18-SDS 3 |

| HOURLY OPERATIONS SUMMARY (000-2400hrs) | OPERATIONS BREAKDOWN |
| --- | --- |
| FROM | TO | OPERATION |  |  |
| 00:00 | 01:00 | Drilled 156mm hole 1849-1854m | Drilling | 10.50 |
| 01:00 | 02:00 | Changed out Washpipe in Swivel | Tripping | 3.00 |
| 02:00 | 10:30 | Drilled 156mm hole 1854-1891m | Surveys | 1.00 |
| 10:30 | 11:00 | Circulated | Reaming |  |
| 11:00 | 12:00 | Ran survey at 1880m | Slip & Cut Block Line | 1.00 |
| 12:00 | 13:00 | Drilled 156mm hole 1891-1898 | Circulate & Clean Hole | 1.50 |
| 13:00 |  | Mud flow between 178mm Casing | Cement Casing |  |
|  |  | and the 245mm Casing indicated | Rig Repair | 1.00 |
|  | 14:00 | hole in Casing -ceased drilling | Surveys |  |
| 14:00 | 17:00 | Tripped out to surface | Run Casing |  |
| 17:00 | 18:00 | Slipped and cut block line | Rig Service |  |
| 18:00 |  | Scientific Drilling loggers located hole | Test BOP’s |  |
|  | 24:00 | in Casing at 121m | Drill Out Cement |  |
|  |  |  | Logging | 6.00 |
|  |  |  | W.O.C. |  |
|  |  |  | Cement Plug |  |
|  | JSA | Changing out the washpipe |  |  |
|  |  | Days Since Last LTA: 367 |  |  |

| BIT INFORMATION | MUD PROPERTIES |
| --- | --- |
| Bit Number | 9 Run # 12 |  | Density (ppg) | 9.20 |
| Size (mm) | 156 |  | Viscosity (Sec) | 45 |
| Make | Reed |  | PV @ Degree C | 15 |
| Type | SL51HP |  | YP (lbs/100ft2) | 10 |
| IADC Code | 4-3-7 |  | API Filtrate (ml/30min) | 7.0 |
| Serial Number | HP5998 |  | Gels (lbs/100ft2) | 2 / 3 /4 |
| Nozzles (x32) | 16-16-13 |  | Filter Cake (32nds inch) | 1/- |
| Depth In (m) | 1643 |  | Sand (% Vol) | 0.10 |
| Depth Out (m) | 1898 |  | Solids (% Vol) | 7.5 |
| Total Metres | 251 |  | Hardness (Ca mg/l) | 140 |
| Hours | 50.5 |  | KCl (% by wt) | 1.50 |
| WOB (kg) | 7000 |  | Chlorides (Mg/l) | 9,400 |
| RPM | 100 |  | Methyl Blue (ppg eq) | 7.5 |
| Condition | 2-2-RG-G-E | I-N0-HP | Potassium (Mg/l) | 8,000 |
| Impact Force | 118lb/ft |  | Daily Cost ($) | 1,523 |
| Jet Velocity | 122 ft/sec |  | Cumulative Cost ($) | 44,309 |

LAKES OIL N.L.

DAILY DRILLING REPORT NO.                       PAGE: 2

| CEMENT DATA | LAST CASING | CHEMICALS USED |
| --- | --- | --- |
| Sacks |  | Size | 178 mm | Starlose | 1 |
| Class |  | Weight | 38.69 | Xanthum Gum XCD | 2 |
|  |  | Grade | N-80 | Barite | 14 |
|  |  | Connection | Buttress | Caustic | 1 |
|  |  | Joints | 92 | Potassium Chloride | 10 |
|  |  | Length | 1092.15m | Cepac-R | 1 |
|  |  | Shoe | 1097.00 | Sodium Bicarbonate | 1 |
|  |  |  |  | Sodium Sulphite | 1 |
|  |  |  |  | AMC Defoamer | 3 |

| SURVEYS | PUMP No.1 | PUMP No.2 |
| --- | --- | --- |
| 7.00 deg at | 1282 m | Liner | 140mm | Liner |  |
| 8.00 deg at | 1346 m | Stroke | 16 inch | Stroke |  |
| 8.00 deg at | 1387 m | Pressure | 8970kpa | Pressure |  |
| 8.50 deg at | \ m | A.V. DP | 192 ft/min | A.V. DP |  |
| 8.50 deg at | 1452 m | A.V. DC | 281 ft/min | A.V. DC |  |
| 9.00 deg at | 1489m m | SPM | 40 | SPM |  |
| 9.50 deg at | 1575 m | GPM | 198 | GPM |  |
| 7.9 deg at | 1880 m |  |  |  |  |
| deg at | m |  |  |  |  |

BHA: Bit-Bit sub- 2 x 4-3/4 Drill collars-Stabilizer-11 x 4-3/4 Drill collars-Jar-2 x 4-3/4 Drill collars

COMMENTS:

REPORT BY: Lou De-Vattimo