LAKES OIL N.L.

DAILY DRILLING REPORT

| WELL: Boundary Crk-2 | REPORT No.: 33 | DATE: 11-11-05 |
| --- | --- | --- |
| DFS: 32 | 2400 DEPTH: 2161 | Last Depth: 2135 |
| 24hr Progress: 26 | PTD: 2500 | Total Fuel: 8900 |
| Fuel Usage: 2400 | Daily Cost: 34,796 | Cum Cost: 1,674,914 |
| 0600hrs Operation: Drilling 156mm hole at 2177m |
| Next 24hr Operation: Drill ahead with 156mm Bit - |
| Site Personnel: Lakes 3-AMC 1-Higgins 2-Hunt 17 |

| HOURLY OPERATIONS SUMMARY (000-2400hrs) | OPERATIONS BREAKDOWN |
| --- | --- |
| FROM | TO | OPERATION |  |  |
| 00:00 | 07:30 | Drilled 156mm hole 2135 to 2158 | Drilling | 9.50 |
| 07:30 | 08:00 | Circulated | Tripping | 11.50 |
| 08:00 | 09:00 | Ran survey at 2146m | Surveys |  |
| 09:00 | 14:30 | Tripped out for Bit change | Reaming |  |
| 14:30 | 15:00 | Serviced the Rig | Slip & Cut Block Line | 1.00 |
| 15:00 | 16:00 | Slipped and cut Block line | Circulate & Clean Hole | 0.50 |
| 16:00 | 22:00 | Tripped in hole with new Bit | Cement Casing |  |
| 22:00 | 24:00 | Drilled 156mm hole 2158m to 2161m | Rig Repair |  |
|  |  |  | Surveys | 1.00 |
|  |  |  | Run Casing |  |
|  |  |  | Rig Service | 0.50 |
|  |  |  | Test BOP’s |  |
|  |  |  | Drill Out Cement |  |
|  |  |  | Logging |  |
|  |  |  | W.O.C. |  |
|  |  |  | Cement Plug |  |
|  | JSA | Tool maintenance | Wait on Cementer |  |
|  |  | Slip and cut block line | Made up fishing tools |  |
|  | 373 | Days Since Last LTA: |  |  |

| BIT INFORMATION | MUD PROPERTIES |
| --- | --- |
| Bit Number | 15 Bit #10 | 14 Bit # 9 | Density (ppg) | 9.60 |
| Size (mm) | 156 | 156 | Viscosity (Sec) | 44 |
| Make | Reed | Reed | PV @ Degree C | 18 |
| Type | SL53AK | SL51HP | YP (lbs/100ft2) | 14 |
| IADC Code | 5-3-7 | 5-1-7 | API Filtrate (ml/30min) | 6.6 |
| Serial Number | NE2276 | HP5997 | Gels (lbs/100ft2) | 3 / 4 / 8 |
| Nozzles (x32) | 13-14-16 | 13-14-16 | Filter Cake (32nds inch) | 1/- |
| Depth In (m) | 2158 | 1974 | Sand (% Vol) | 0.10 / 0.20 |
| Depth Out (m) |  | 2158 | Solids (% Vol) | 9.4 |
| Total Metres | 3 | 184 | Hardness (Ca mg/l) | 420 |
| Hours | 2.00 | 49,50 | KCl (% by wt) | 1.83 |
| WOB (kg) | 4000 | 8000 | Chlorides (Mg/l) | 10500 |
| RPM | 90 | 90 | Methyl Blue (ppg eq) | 9.00 |
| Condition |  | 8-8-LT-A-8-2-JD-TQ | Potassium (Mg/l) | 9,300 |
| Impact Force |  | 116ft/lb | Daily Cost ($) | 919 |
| Jet Velocity |  | 127ft/sec | Cumulative Cost ($) | 49,584 |

LAKES OIL N.L.

DAILY DRILLING REPORT NO. 33                 PAGE: 2

| CEMENT DATA | LAST CASING | CHEMICALS USED |
| --- | --- | --- |
| Sacks |  | Size | 178 mm | Starlose | 2 |
| Class |  | Weight | 38.69 | Xanthum Gum XCD | 1 |
|  |  | Grade | N-80 | Caustic | 1 |
|  |  | Connection | Buttress | Xtra sweep | 5 |
|  |  | Joints | 92 | Baracarb 10 | 2 |
|  |  | Length | 1092.15m | Baracarb 20 | 4 |
|  |  | Shoe | 1097.00 | Baracarb 50 | 14 |
|  |  |  |  | Sodium Bicarbonate | 2 |
|  |  |  |  | Sodium Sulphite | 2 |

| SURVEYS | PUMP No.1 | PUMP No.2 |
| --- | --- | --- |
| 6.4 deg at | 2146 m | Liner | 140mm | Liner |  |
| 8.00 deg at | 1346 m | Stroke | 16 inch | Stroke |  |
| 8.00 deg at | 1387 m | Pressure | 8970kpa | Pressure |  |
| 8.50 deg at | 1415 m | A.V. DP | 192 ft/min | A.V. DP |  |
| 8.50 deg at | 1452 m | A.V. DC | 281 ft/min | A.V. DC |  |
| 9.00 deg at | 1489m m | SPM | 40 | SPM |  |
| 9.50 deg at | 1575 m | GPM | 198 | GPM |  |
| 7.9 deg at | 1880 m |  |  |  |  |
| 8.00 deg at | 1956 m |  |  |  |  |

BHA: Bit - Junk sub- -Bit sub- 2 x 4-3/4 Drill collars-11 x 4-3/4 Drill collars-Jar-2 x 4-3/4 Drill collar

COMMENTS: Pulled previous bit because of torque and drill rate drop

REPORT BY: Lou De-Vattimo