LAKES OIL N.L.

DAILY DRILLING REPORT

| WELL: Boundary Creek No.2 | REPORT No.: 34 | DATE: 12-11-2005 |
| --- | --- | --- |
| DFS: 33 | 2400 DEPTH: 2193m | Last Depth: 2161m |
| 24hr Progress: 32m | PTD: 2500m | Total Fuel: 7,400 |
| Fuel Usage: 1,500 | Daily Cost : 27,401 | Cum Cost: $1,702,315 |
| 0600hrs Operation: | Drilling 152.4mm hole at 2206m |
| Next 24hr Operation: | Drill ahead with 152.4mm hole |
| Site Personnel: | Lakes 3, AMC 1, Higgins 2, Hunt 17 |

| HOURLY OPERATIONS SUMMARY (000-2400hrs) | OPERATIONS BREAKDOWN |
| --- | --- |
| FROM | TO | OPERATION | Drilling | 13.00 |
| 00:00 | 13:00 | Drilled 156mm hole 2161- 2193m | Tripping | 10.00 |
| 13:00 | 18:00 | Tripped out for Bit change due to slow drill rate | Surveys |  |
| 18:00 | 19:00 | Changed out the Kelly bushing rollers | Reaming |  |
| 19:00 | 24:00 | Made up new 152.4mm Bit tripped in to 1073m | Slip & Cut Block Line |  |
|  |  |  | Circulate & Clean Hole |  |
|  |  |  | Cement Casing |  |
|  |  |  | Rig Repair | 1.00 |
|  |  |  | Surveys |  |
|  |  |  | Run Casing |  |
|  |  |  | Rig Service |  |
|  |  |  | Test BOP’s |  |
|  |  |  | Drill Out Cement |  |
|  |  |  | Logging |  |
|  |  |  | W.O.C. |  |
|  |  |  | Cement Plug |  |
|  |  |  | Wait on Cementer |  |
|  |  |  | Make up Fishing Tools |  |

| BIT INFORMATION | MUD PROPERTIES |
| --- | --- |
| Bit Number | 5 | 6 | Density (ppg) | 9.6 |
| Run Number | 15 | 16 | Viscosity (Sec) | 42 |
| Size (mm) | 156 | 152.4 | PV @ Degree C | 17 |
| Make | Reed | Reed | YP (lbs/100ft2) | 14 |
| Type | SL53AK | SL43HKPR | API Filtrate (ml/30min) | 7.2 |
| IADC Code | 5-3-7 | 4-3-7 | Gels (lbs/100ft2) | 3/5/8 |
| Serial Number | NE2276 | HY2709 | Filter Cake (32nds inch) | 1/- |
| Nozzles (x32) | 13-14-16 | 13-14-16 | Sand (% Vol) | 0.10/0.20 |
| Depth In (m) | 2158 | 2193 | Solids (% Vol) | 8.6 |
| Depth Out (m) | 2193 |  | Hardness (Ca mg/l) | 280 |
| Total Meters | 35 |  | KCl (% by wt) | 1.83 |
| Hours | 15 |  | Chlorides (Mg/l) | 10,200 |
| WOB (kg) | 8,000 |  | Methyl Blue (ppg eq) | 8.5 |
| RPM | 90 |  | Potassium (Mg/l) | 9,700 |
| Condition | 0-0-N0-A-E-I | -NO-PR | Daily Cost ($) | 524 |
| Impact Force | 118lb/ft |  | Cumulative Cost ($) | 50,110 |
| Jet Velocity | 127ft/sec |  |  |  |

LAKES OIL N.L.

DAILY DRILLING REPORT NO.    34

| CEMENT DATA | LAST CASING | CHEMICALS USED |
| --- | --- | --- |
| Sacks |  | Size | 178mm | Starlose | 1 |
| Class |  | Weight | 38.69 | Xanthum Gum (XCD) | 1 |
|  |  | Grade | N-80 | Caustic | 1 |
|  |  | Connection | Buttress | Cepac-R | 2 |
|  |  | Joints | 92 | Baracarb 10 |  |
|  |  | Length | 1092.15m | Baracarb 20 | 11 |
|  |  | Shoe | 1097.00m | Baracarb 50 |  |
|  |  |  |  | Sodium Sulphite | 2 |

| SURVEYS | PUMP No.1 | PUMP No.2 |
| --- | --- | --- |
| 9.5 degrees at 1575m | Liner | 140 mm | Liner |  |
| 7.9 degrees at 1880m | Stroke | 16 inch | Stroke |  |
| 8.0 degrees at 1956m | Pressure | 8,970 KPA | Pressure |  |
| 6.4 degrees at 2146m | A.V. DP | 192 ft/min | A.V. DP |  |
|  | A.V. DC | 281 ft/min | A.V. DC |  |
|  | SPM | 40 | SPM |  |
|  | GPM | 198 | GPM |  |

OCCUPATIONAL HEALTH AND SAFETY

| BHA: | Bit-Junk Sub - 2x4¾75” Drill Collars - 14x4¾” Drill Collars – Jars - 2x4¾” Drill Collars |
| --- | --- |
| DAYS SINCE LAST LTA: | 374 |
| COMMENTS: | Pulled previous bit due to drill rate drop |
| REPORT BY: | Lou De-Vattimo |