LAKES OIL N.L.

DAILY DRILLING REPORT

| WELL: Boundary Creek No.2 | REPORT No.: 36 | DATE: 14-11-2005 |
| --- | --- | --- |
| DFS: 35 | 2400 DEPTH: 2271m | Last Depth: 2271m |
| 24hr Progress: 0m | PTD: 2500m | Total Fuel: 3,600 |
| Fuel Usage: 2,000 | Daily Cost : $ 33,395 | Cum Cost: $1,769,587 |
| 0600hrs Operation: | Drilling 152.40mm hole at 2277m |
| Next 24hr Operation: | Drill ahead with possible trip for Bit change |
| Site Personnel: | Lakes 3, AMC 1, Higgins 2, Hunt 18 |

| HOURLY OPERATIONS SUMMARY (000-2400hrs) | OPERATIONS BREAKDOWN |
| --- | --- |
| FROM | TO | OPERATION | Drilling |  |
| 00:00 | 04:30 | Tripped out due to torque down-hole | Tripping | 21.50 |
| 04:30 | 05:00 | Serviced the rig | Surveys |  |
| 05:00 | 06:00 | Slipped and cut Block line | Reaming |  |
| 06:00 | 06:30 | Made up reverse circulation junk basket | Slip & Cut Block Line | 1.00 |
| 06:30 | 13:00 | Tripped in hole to fish for drill bit cone | Circulate & Clean Hole |  |
| 13:00 | 19:00 | Fished for cone then tripped out | Cement Casing |  |
| 19:00 | 20:00 | Recovered cone then made up drill bit | Rig Repair |  |
| 20:00 | 24:00 | Tripped in hole | Surveys |  |
|  |  |  | Run Casing |  |
|  |  |  | Rig Service | 0.50 |
|  |  |  | Test BOP’s |  |
|  |  |  | Drill Out Cement |  |
|  |  |  | Logging |  |
|  |  |  | W.O.C. |  |
|  |  |  | Cement Plug |  |
|  |  |  | Wait on Cementer |  |
|  |  |  | Make up Fishing Tools | 1.00 |

| BIT INFORMATION | MUD PROPERTIES |
| --- | --- |
| Bit Number | 6 | 7 | Density (ppg) | 9.65 |
| Run Number | 16 | 17 | Viscosity (Sec) | 45 |
| Size (mm) | 152.4 | 152.4 | PV @ Degree C | 17 |
| Make | Reed | Reed | YP (lbs/100ft2) | 15 |
| Type | SL43HKPR | SL12TKPR | API Filtrate (ml/30min) | 7.4 |
| IADC Code | 4-3-7 | 1-2-7 | Gels (lbs/100ft2) | 3/7/8 |
| Serial Number | HY2709 | NR2615 | Filter Cake (32nds inch) | 1/- |
| Nozzles (x32) | 13-14-16 | 13-14-16 | Sand (% Vol) | 0.10/0.25 |
| Depth In (m) | 2193 | 2271 | Solids (% Vol) | 9.7 |
| Depth Out (m) | 2271 |  | Hardness (Ca mg/l) | 100 |
| Total Meters | 78 |  | KCl (% by wt) | 1.83 |
| Hours | 21.50 |  | Chlorides (Mg/l) | 10,000 |
| WOB (kg) | 8,000 |  | Methyl Blue (ppg eq) | 10.5 |
| RPM | 90 |  | Potassium (Mg/l) | 9,700 |
| Condition | 88LC182JDT |  | Daily Cost ($) | 128 |
| Impact Force |  |  | Cumulative Cost ($) | 51,731 |
| Jet Velocity |  |  |  |  |

LAKES OIL N.L.

DAILY DRILLING REPORT NO.    36

| CEMENT DATA | LAST CASING | CHEMICALS USED |
| --- | --- | --- |
| Sacks |  | Size | 178mm | Baracarb-20 | 14 |
| Class |  | Weight | 38.69 | Baracarb-25 | 26 |  | Grade | N-80 |  |  | Connection | Buttress |  |  |
|  |  | Joints | 92 |  |  |
|  |  | Length | 1092.15m |  |  |
|  |  | Shoe | 1097.00m |  |  |
|  |  |  |  |  | 2 |  |  |  |  | 2 |
|  |  |  |  |  | 4 |
|  |  |  |  |  | 9 |
|  |  |  |  |  | 2 |
| SURVEYS | PUMP No.1 | PUMP No.2 |
| 9.5 degrees at 1575m | Liner | 140 mm | Liner |  |
| 7.9 degrees at 1880m | Stroke | 16 inch | Stroke |  |
| 8.0 degrees at 1956m | Pressure | 8,970 KPA | Pressure |  |
| 6.4 degrees at 2146m | A.V. DP | 192 ft/min | A.V. DP |  |
|  | A.V. DC | 281 ft/min | A.V. DC |  |
|  | SPM | 40 | SPM |  |
|  | GPM | 198 | GPM |  |

OCCUPATIONAL HEALTH AND SAFETY

| BHA: | Bit-Junk Sub - 2x4¾75” Drill Collars - 14x4¾” Drill Collars – Jars - 2x4¾” Drill Collars |
| --- | --- |
| DAYS SINCE LAST LTA: | 376 |
| COMMENTS: | Slow drill rate due to hard formation |
| REPORT BY: | Lou De-Vattimo |