LAKES OIL N.L.

DAILY DRILLING REPORT

| WELL: Boundary Creek No.2 | REPORT No.: 38 | DATE: 16-11-2005 |
| --- | --- | --- |
| DFS: 37 | 2400 DEPTH: 2323m | Last Depth: 2288m |
| 24hr Progress: 35m | PTD: 2500m | Total Fuel: 10,400lt |
| Fuel Usage: 1,800lt | Daily Cost : $28,622 | Cum Cost: $1,829,751 |
| 0600hrs Operation: | Changing drill bit then trip in hole |
| Next 24hr Operation: | Drill ahead |
| Site Personnel: | Lakes 3, AMC 1, Higgins 2, Hunt 19 |

| HOURLY OPERATIONS SUMMARY (000-2400hrs) | OPERATIONS BREAKDOWN |
| --- | --- |
| FROM | TO | OPERATION | Drilling | 23.50 |
| 00:00 | 23:30 | Drilled 152.4mm hole from 2288m to 2323m | Tripping |  |
| 23:30 | 24:00 | Pumped pill to trip out for Bit change | Surveys |  |
|  |  |  | Reaming |  |
|  |  |  | Slip & Cut Block Line |  |
|  |  |  | Circulate & Clean Hole | 0.50 |
|  |  |  | Cement Casing |  |
|  |  |  | Rig Repair |  |
|  |  |  | Surveys |  |
|  |  |  | Run Casing |  |
|  |  |  | Rig Service |  |
|  |  |  | Test BOP’s |  |
|  |  |  | Drill Out Cement |  |
|  |  |  | Logging |  |
|  |  |  | W.O.C. |  |
|  |  |  | Cement Plug |  |
|  |  |  | Wait on Cementer |  |
|  |  |  | Make up Fishing Tools |  |

| BIT INFORMATION | MUD PROPERTIES |
| --- | --- |
| Bit Number |  | 8 | Density (ppg) | 9.35 |
| Run Number |  | 18 | Viscosity (Sec) | 40 |
| Size (mm) |  | 152.4 | PV @ Degree C | 12 |
| Make |  | Reed | YP (lbs/100ft2) | 13 |
| Type |  | SL53ADHTP | API Filtrate (ml/30min) | 7.4 |
| IADC Code |  | 5-3-7 | Gels (lbs/100ft2) | 2 / 4 / 7 |
| Serial Number |  | MX8935 | Filter Cake (32nds inch) | 1/- |
| Nozzles (x32) |  | 13-14-20 | Sand (% Vol) | 0.10 |
| Depth In (m) |  | 2285 | Solids (% Vol) | 9.0 |
| Depth Out (m) |  | 2323 | Hardness (Ca mg/l) | 80 |
| Total Meters |  | 28 | KCl (% by wt) | 1.58 |
| Hours |  | 25.5 | Chlorides (Mg/l) | 9,900 |
| WOB (kg) |  | 8000 | Methyl Blue (ppg eq) | 6.5 |
| RPM |  | 80 | Potassium (Mg/l) | 8,000 |
| Condition |  |  | Daily Cost ($) | 1,855 |
| Impact Force |  | 89lb/ft | Cumulative Cost ($) | 54,362 |
| Jet Velocity |  | 100ft/sec |  |  |

LAKES OIL N.L.

DAILY DRILLING REPORT NO.    38

| CEMENT DATA | LAST CASING | CHEMICALS USED |
| --- | --- | --- |
| Sacks |  | Size | 178mm | AMC Defoamer | 3 |
| Class |  | Weight | 38.69 | Biocide | 1 |
|  |  | Joints | 92 | Barite | 14 |
|  |  | Length | 1092.15m | Caustic | 1 |
|  |  | Shoe | 1097.00m | Sodium sulphite | 2 |
|  |  |  |  | Sodium Bicarbonate | 2 |
|  |  |  |  | Sodium Sulphite | 2 |
|  |  |  |  | Potassium Chloride | 10 |
|  |  |  |  | Xanthum gum | 3 |
| SURVEYS | PUMP No.1 | PUMP No.2 |
| 9.5 degrees at 1575m | Liner | 140 mm | Liner |  |
| 7.9 degrees at 1880m | Stroke | 16 inch | Stroke |  |
| 8.0 degrees at 1956m | Pressure | 8,970 KPA | Pressure |  |
| 6.4 degrees at 2146m | A.V. DP | 192 ft/min | A.V. DP |  |
|  | A.V. DC | 281 ft/min | A.V. DC |  |
|  | SPM | 38 | SPM |  |
|  | GPM | 188 | GPM |  |

OCCUPATIONAL HEALTH AND SAFETY

| BHA: | Bit-Junk Sub - 2x4¾75” Drill Collars - 14x4¾” Drill Collars – Jars - 2x4¾” Drill Collars |
| --- | --- |
| DAYS SINCE LAST LTA: | 378 |
| COMMENTS: | Slow drill rate due to hard formation |
| REPORT BY: | Lou De-Vattimo |