LAKES OIL N.L.

DAILY DRILLING REPORT

| WELL: Boundary Creek No.2 | REPORT No.: 44 | DATE: 23-11-2005 |
| --- | --- | --- |
| DFS: 43 | 2400 DEPTH: 2341m | Last Depth: 2341m |
| 24hr Progress: 0m | PTD: 2500m | Total Fuel: 4,500 |
| Fuel Usage: 600 | Daily Cost : $ 410,015 | Cum Cost: $2,531,189 |
| 0600hrs Operation: | Contractor rigging down Rig off payroll at midnight 23-11-05 |
| Next 24hr Operation: |  |
| Site Personnel: | Lakes 2 , Hunt 17 , Baker Atlas 6 ,Halliburton 3 |

| HOURLY OPERATIONS SUMMARY (000-2400hrs) | OPERATIONS BREAKDOWN |
| --- | --- |
| FROM | TO | OPERATION | Drilling |  |
| 00:00 | 03:30 | Layed out excess drill pipe | Tripping | 10.50 |
| 03:30 | 04:00 | Layed out the Kelly spinner | Surveys |  |
| 04:00 | 05:00 | Ran 30 stands drill pipe in hole | Reaming |  |
| 05:00 | 05:30 | Cleared rig floor for laying out pipe | Slip & Cut Block Line |  |
| 05:30 | 10:30 | Layed out pipe to 132m | Circulate & Clean Hole |  |
| 10:30 | 11:30 | Set 12bbl cement plug from 132m to surface | Cement Casing |  |
| 11:30 | 12:00 | Layed out pipe | Rig Repair |  |
| 12:00 | 13:00 | Layed Out Kelly-Mousehole | Surveys |  |
| 13;00 | 23:00 | Removed the BOP and all associated equipment | Run Casing |  |
| 23:00 | 24:00 | Secured well with suspension cap | Rig Service |  |
|  |  |  | Test BOP’s |  |
|  |  | Released the Rig | Drill Out Cement |  |
|  |  |  | Logging |  |
|  |  |  | W.O.C. |  |
|  |  |  | Cement Plug | 1.150 |
|  |  |  | Wait on Cementer |  |
|  |  |  | Make up Fishing Tools |  |
|  |  |  | Rig Down |  |

| BIT INFORMATION | MUD PROPERTIES |
| --- | --- |
| Bit Number |  |  | Density (ppg) |  |
| Run Number |  |  | Viscosity (Sec) |  |
| Size (mm) |  |  | PV @ Degree C |  |
| Make |  |  | YP (lbs/100ft2) |  |
| Type |  |  | API Filtrate (ml/30min) |  |
| IADC Code |  |  | Gels (lbs/100ft2) |  |
| Serial Number |  |  | Filter Cake (32nds inch) |  |
| Nozzles (x32) |  |  | Sand (% Vol) |  |
| Depth In (m) |  |  | Solids (% Vol) |  |
| Depth Out (m) |  |  | Hardness (Ca mg/l) |  |
| Total Meters |  |  | KCl (% by wt) |  |
| Hours |  |  | Chlorides (Mg/l) |  |
| WOB (kg) |  |  | Methyl Blue (ppg eq) |  |
| RPM |  |  | Potassium (Mg/l) |  |
| Condition |  |  | Daily Cost ($) |  |
| Impact Force |  |  | Cumulative Cost ($) |  |
| Jet Velocity |  |  |  |  |

LAKES OIL N.L.

DAILY DRILLING REPORT NO.    43

| CEMENT DATA | LAST CASING | CHEMICALS USED |
| --- | --- | --- |
| Sacks |  | Size | 178mm |  |  |
| Class |  | Weight | 38.69 |  |  |
|  |  | Joints | 92 |  |  |
|  |  | Length | 1092.15m |  |  |
|  |  | Shoe | 1097.00m |  |  |
| SURVEYS | PUMP No.1 | PUMP No.2 |
|  | Liner | 140 mm | Liner |  |
|  | Stroke | 16 inch | Stroke |  |
|  | Pressure |  | Pressure |  |
|  | A.V. DP |  | A.V. DP |  |
|  | A.V. DC |  | A.V. DC |  |
|  | SPM |  | SPM |  |
|  | GPM |  | GPM |  |

| OCCUPATIONAL HEALTH AND SAFETY |
| --- |
| Running cement plugs |  |  |

| BHA: |  |
| --- | --- |
| DAYS SINCE LAST LTA: | 385 |
| COMMENTS: | Loaded out some of Baker Atlas equipment |
| REPORT BY: | Lou De-Vattimo |