LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Boundary creek-2 | REPORT No. : | 6 | DFS: | 5 | DATE : | 15-Oct-05 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 261m | LAST DEPTH : | 132m | 24 HR PROGRESS : | 0m | PTD : | 2500m |
| TOTAL FUEL : | 12,900 | FUEL USAGE : | 1,300 |  | 64,496 | CUM. COST : $ | 406,647 |
| 0600 OPS : | Pick up Kelly to drill out shoetrack |
| Next 24 hr OPS: | Drill ahead with 216mm bit from 261m |
| Site Personnel: | Lakes 3- A.M.C 1- Mud logger 2- Hunt Energy 20- Atlas loggers 3 |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 2 Re run |  |  | Drilling |  |  | Density | 8.55 | ppg |
| Size (mm) | 216mm |  |  | Tripping |  |  | Viscosity | 42 | Sec |
| Make | Reed |  |  | Surveys |  |  | PV @ Deg C | 15 | Deg C |
| Type | ETH 11 |  |  | Reaming |  |  | YP lbs/100 ft 2 | 24 | Lbs/100ft |
| IADC Code | 1-1-7 |  |  | Slip and cut block line |  |  | API Filtrate | 10.0 | m/30min |
| Serial Number | MX-8867 |  |  | Circulate and clean hole |  |  | Gels lbs/100 ft 2 | 3 / 3 |  |
| Nozzles (32) | 13-13-13 |  |  | Cement casing |  |  | Cake 32nds/ in | 1 |  |
| Depth in (m) | 261 |  |  | Rig repair |  |  | Sand |  | % Vol |
| Depth out (m) |  |  |  | Surveys |  |  | Solids | 1.0 | % Vol |
| Total Metres |  |  |  | Run Casing |  |  | Hardness Ca mg/l | 70 |  |
| Hours |  |  |  | Rig Service |  |  | KCL Concentration | 1.33 | % by wt |
| WOB (kg) |  |  |  | Nipple up BOP | 18.50 |  | Chlorides | 9,000 | Mg/l |
| RPM |  |  |  | Drill out Cmt |  |  | Methyl Blue |  | Ppb equiv |
| Condition |  |  |  | Logging |  |  | K+ | 7,100 | Mg/l |
| Impact Force |  |  |  | W.0.C | 5.50 |  | Daily Cost $ | 2,299 |
| Jet Velocity |  |  |  | Cement plug |  |  | Cum Cost $ | 8,450 |
| B.H.A.: | Bit- Bit sub- 2 x 6-1/4inch drill collars- stabilizer -6 x 6-1/4inch drill collars -4 x Hevi-Wate drillpipe |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 0.25 | ° at | 218m | m |  | Type | Amount |
| 00:00 | 05:30 | W.O.C |  |  | ° at |  | m |  | AMC Biocide | 1 |
| 05:30 |  | Layed out riser joint and landing joint and cleared |  |  | ° at |  | m |  | AMC Defoamer | 1 |
|  | 08:30 | out casing handling equipment |  |  | ° at |  | m |  | AMC PAC-R | 6 |
| 08:30 |  | Installed and made up Casing bowl-wellhead spools |  |  | ° at |  | m |  | Caustic | 1 |
|  | 12:00 | and the Blowout preventor |  |  | ° at |  | m |  | Potassium chloride | 24 |
| 12;00 | 19:00 | Made up the BOP and all associated equipment |  |  | ° at |  | m |  | Starlose | 12 |
| 19:00 | 24:00 | Tested BOP using Halliburton |  |  | ° at |  | m |  |  |  |
|  |  |  |  | PUMP 1 |  | PUMP 2 |
|  |  |  |  | Liner | 140 | mm |  | Liner | 140 | mm |
|  |  |  |  | Pressure |  | kPa |  | Pressure |  | KPa |
|  |  |  |  | A.V. DP |  | m/min |  | A.V. DP |  | m/min |
|  |  |  |  | A.V. DC |  | m/min |  | A.V. DC |  | m/min |
|  |  |  |  | SPM |  |  | SPM |  |
|  |  |  |  | GPM |  |  | GPM |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks |  |  | Size | 244mm |  |
|  |  |  |  | Class |  |  | Weight | 53.57 | Kg/m |
|  |  |  |  |  |  |  |  | Grade | K-55 |  |
|  |  |  |  |  |  |  |  | Connection | Buttress |  |
|  | JSA | Nipple up the BOP |  |  |  |  |  | Joints | 21 |  |
|  |  |  |  |  |  |  |  | Length | 253 | m |
| Days since | LTA | 347 |  |  |  |  | Shoe | 258 | m |

,66