LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Boundary creek-2 | REPORT No. : | 13 | DFS: | 12 | DATE : | 22 Oct-05 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 1100m | LAST DEPTH : | 1082m | 24 HR PROGRESS : | 18m | PTD : | 2500m |
| TOTAL FUEL : | 9,400 | FUEL USAGE : | 600 |  | 25,849 | CUM. COST : $ | 631,937 |
| 0600 OPS : | Running 177.8mm Casing |
| Next 24 hr OPS: | Run casing to 1100m-cement same-install “B” section of wellhead |
| Site Personnel: | Lakes 3 A.M.C 1- Mud logger 2- Hunt Energy 18- Atlas loggers 6 |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number |  |  |  | Drilling |  |  | Density | 9.60 | ppg |
| Size (mm) |  |  |  | Tripping | 12.00 |  | Viscosity | 40 | Sec |
| Make |  |  |  | Surveys |  |  | PV @ Deg C | 13 | Deg C |
| Type |  |  |  | Reaming |  |  | YP lbs/100 ft 2 | 6 | Lbs/100ft |
| IADC Code |  |  |  | Slip and cut block line | 1.00 |  | API Filtrate |  | m/30min |
| Serial Number |  |  |  | Circulate and clean hole | 2.00 |  | Gels lbs/100 ft 2 | 4 / 8 /11 |  |
| Nozzles (32) |  |  |  | Cement casing |  |  | Cake 32nds/ in | 1 |  |
| Depth in (m) |  |  |  | Rig repair |  |  | Sand | 0.15 | % Vol |
| Depth out (m) |  |  |  | Surveys |  |  | Solids | 10.00 | % Vol |
| Total Metres |  |  |  | Run Casing |  |  | Hardness Ca mg/l | 60 |  |
| Hours |  |  |  | Rig Service |  |  | KCL Concentration | 1.25 | % by wt |
| WOB (kg) |  |  |  | Test BOP |  |  | Chlorides | 8,800 | Mg/l |
| RPM |  |  |  | Drill out Cmt |  |  | Methyl Blue | 15.8 | Ppb equiv |
| Condition |  |  |  | Logging | 9.00 |  | K+ | 6,600 | Mg/l |
| Impact Force |  |  |  | W.0.C |  |  | Daily Cost $ | 732 |
| Jet Velocity |  |  |  | Cement plug |  |  | Cum Cost $ | 24,575 |
| B.H.A.: | Bit- Bit sub- 2 x 6-1/4inch drill collars- stabilizer -6 x 6-1/4inch drill collars-Jars-2 x 6-1/4 inch drill collars -4 x Hevi-Wate drillpipe |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 0.25 | ° at | 218m | m |  | Type | Amount |
| 00:00 | 07:30 | Baker Atlas ran log # 2 R-Core |  | 1.50 | ° at | 600m | m |  | Caustic | 1 |
| 07:30 | 09:00 | Layed out tools and rigged down logger |  | 2.00 | ° at | 797m | m |  | Citric acid | 1 |
| 09:00 | 10:00 | Slipped and cut block line |  | 2.50 | ° at | 938m | m |  | AMC PAC-L |  |
| 10:00 | 14:00 | Wiper tripped in hole to bottom at 1100m |  | 3.00 | ° at | 1096m | m |  | Barite | 26 |
| 14:00 | 16:00 | Circulated and conditioned mud |  |  | ° at |  | m |  | Potassium chloride |  |
| 16:00 | 24:00 | Layed out the 4-1/2 drillpipe string |  |  | ° at |  | m |  | Soium Bicarbonate |  |
|  |  |  |  |  | ° at |  | m |  | Sodium sulphite | 1 |
|  |  |  |  | PUMP 1 |  | PUMP 2 |
|  |  | Total Casing on site 96 lengths |  | Liner | 140 | mm |  | Liner | 140 | mm |
|  |  |  |  | Pressure |  | kPa |  | Pressure |  | KPa |
|  |  |  |  | A.V. DP |  | m/min |  | A.V. DP |  | m/min |
|  |  |  |  | A.V. DC |  | m/min |  | A.V. DC |  | m/min |
|  |  |  |  | SPM |  |  | SPM |  |
|  |  |  |  | GPM |  |  | GPM |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  | Third load of drillpipe arrived from Perth today |  | Sacks |  |  | Size | 244mm |  |
|  |  |  |  | Class |  |  | Weight | 53.57 | Kg/m |
|  |  |  |  |  |  |  |  | Grade | K-55 |  |
|  |  |  |  |  |  |  |  | Connection | Buttress |  |
|  | JSA | Slip and cut line- test and reset the crown-omatic |  |  |  |  |  | Joints | 21 |  |
|  |  |  |  |  |  |  |  | Length | 253 | m |
| Days since | LTA | 354 |  |  |  |  | Shoe | 258 | m |

,66