|  | LAKES OIL N.L. (A.C.N. 004 247 214) | Registered Office: Level 11, 500 Collins Street, Melbourne, Vic. 3000 | P.O. Box 300, Collins St. West Melbourne, Vic. 8007 Phone: (03) 9629 1566 Fax: (03) 9629 1624 |
| --- | --- | --- | --- |

# Boundary Creek-2 Wellsite

# via Longford

November 6th 2005

# Boundary Creek-2 Daily Report # 27 – November 6th 2005

24 Hour Progress

At 6am this morning the contractor was preparing to run in the hole open ended and set a cement plug from 220m-180m, having drilled 27m of 156mm hole to a depth of 1898m. At a depth of 1898m mud began returning to the cellar from inside the 244mm casing, suggesting communication to the well bore via a hole in the 178mm casing. The contractor pulled out of the hole and Scientific Drilling ran Suite 2, Run 1 (GR, CCL, PSI, degC, RPS), locating the communication between the casing at a tool joint at 121m. Total gas has ranged from trace-2 units (C1 100%, C2+ 0), no oil fluorescence has been observed during the past 24 hours.

Next 24 Hours

Run in hole open ended to 220m before rigging up the Halliburton cementing unit and setting a cement plug from 220m to 180m. WOC before tagging cement, pumping cement down the annulus and cementing from the casing breach to surface inside the annulus. WOC before changing bit, drilling out cement track to the top of the cement plug and pressure testing. Drill out cement plug and drill ahead in 156mm hole to TD.

Ben Edwards

Lakes Oil