| WELL | BMA A6A |
| --- | --- |
| DATE | 11-02-2006 |
| DAY # | 12 |
| MIDNIGHT ACTIVITY | Drilling ahead. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 3215.0 mMDRT |  | MINIMUM | 0.9 | 3213.0 |
| TVD | 1975.8 mTVDRT |  | MAXIMUM | 90.5 | 3112.0 |
| PROGRESS LAST 24 hrs | 162.0 |  | AVERAGE | 15.9 |  |

|  | TOP (mMDRT) | TOP (mTVDRT) | TOP (mTVDSS) RTtoMSL (32.82m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Kick Off Point | 855.0 | 807.96 | -775.1 |  | 855.0 | 808.0 |
| Lakes Entrance | 961.5 | 908.3 | -875.5 | 1.5 LOW | 960.8 | 906.8 |
| Top of Latrobe | 2779.5 | 1792.3 | -1759.5 | 14.0 LOW | 2735.9 | 1778.3 |
| TCC (N-1 Reservoir) | 3090.0 | 1920.8 | -1888.0 | 1.3 HIGH | 3086.5 | 1922.1 |
| Base of Waste Rock | 3098.5 | 1924.5 | -1891.7 | 4.4 HIGH | 3103.0 | 1928.9 |
| Current OWC |  |  |  |  | 3141.7 | 1944.8 |
| CbF2 horizon | 3138.0 | 1941.7 | -1908.9 | 1.3 HIGH | 3136.1 | 1943.0 |
| CbF1 | 3144.0 | 1944.4 | -1911.6 | 3.0 HIGH | 3146.9 | 1947.4 |
| OOWC |  |  |  |  | 3183.2 | 1961.8 |
| CBSB | 3152.5 | 1948.1 | -1925.3 | 4.3 HIGH | 3160.3 | 1952.4 |
| PKSB |  |  |  |  | 3210.5 | 1973.0 |
| MVSB |  |  |  |  | 3247.0 | 1988.8 |
| Total Depth |  |  |  |  | 3256.4 | 1991.8 |

| Current Formation | LaTrobe: Sandstone, Claystone, Siltstone. |
| --- | --- |

| GAS DATA FCP/FGP | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | iC4 % | nC4 % | C5 % |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAXIMUM | 3139.0 | 137 | 1.683 | 0.171 | 0.085 | 0.015 | 0.029 | 0.022 |
|  | 3138.0 | 659 | 7.441 | 0.736 | 0.516 | 0.094 | 0.190 | 0.126 |
| BACKGROUND |  | 9-20 |  |  |  |  |  |  |
|  |  | 20-50 |  |  |  |  |  |  |
| TRIP GAS | 3197.0 | 59 |  |  |  |  |  |  |
|  | 3197.0 | 117 |  |  |  |  |  |  |

| BIT DATA | PRESENT BIT | LAST BIT |
| --- | --- | --- |
| BIT No. | 1 |  |
| SIZE (in) | 8½ |  |
| MANUFACTURER/TYPE | Smith S73PX |  |
| JETS (/32 inch) | 6 x 20 TFA 1.841 |  |
| DEPTH IN (m) | 851.0 |  |
| DEPTH OUT (m) | IN |  |
| METRES ON RUN (m) | 2364.0 |  |
| HRS ON BTM 24hrs/total | 10.2 / 75.7 |  |
| BIT CONDITION |  |  |
| RPM RANGE LAST 24 hrs | 105-110 TDRPM / 170-175 MMRPM |  |
| Pump Hrs 24 hrs / total | 18.4 / 183.1 |  |
| Krevs 24 hrs / total | 181 / 1124 |  |
| 24 HOUR SUMMARY | Circulate and condition mud, adding Radiagreen - EME. Continue to drill ahead from 3053.0 mMDRT to 3139.0 mMDRT. Circulate hole clean. Continue to drill ahead from 3139.0 mMDRT to 3142.0 mMDRT. Loosing at shakers, reduce pump rate and circulate until shakers clean. Continue to drill ahead from 3142.0 mMDRT to 3197.0 mMDRT. Pressure drop of 200 psi, suspected washout after checking surface equipment. Pull out of to 2308.0 mMDRT, wash out at cross over and last joint of 4" drill pipe. Change out and run in hole to 3197.0 mMDRT. Drill ahead from 3197.0 mMDRT to 3215.0 mMDRT. Circulate and work pipe, while working on pump. |
| 05:00 AM UPDATE 12-02-2006 DEPTH @ 05:00 hours | Drilling ahead. 3226.0 mMDRT (1980.7 mTVDRT) |