WELL NAME: CRC No.1 PERMIT: PPL 13 DAILY GEOLOGICAL REPORT No. 11 DATE: 25/02/2007

Depth: 1323m Progress: 76m Days from Spud: 11

Rig: Century Rig No.11 GL(AHD): 44.8m Drilling Rep: Kevin Murphy/Brian Assels RT: (datum) 50.0m Geologist: David Horner Last Casing: 194mm at 512m

0600 hrs Update: Drill ahead with 171mm hole at 1392m. Current lithology Paaratte Formation, Sandstone (50%) grading to and interbedded with Claystone (50%), background gas 0.001% C1 100%.

Comments: Cut Core No.3, Cut 1246.0-1270.0m (Cut 24.0m, Recovered 8.13m = 34%), RIH with rerun PDC bit, trip gas nil, drill ahead with 171mm hole to 1323m.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1247-1323 | Paaratte Formation - No Show | TG 0.001-0.003% C1 100% C2 Trace C3+ 0 |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Port Campbell Limestone Gellibrand Marl Clifton Formation Narrawaturk Marl Mepunga Formation Dilwyn Formation Pember Mudstone Pebble Point Formation | 5.2 125 462 476 550 635 879 936 | 5.2 122 457 474 551 633 878 939 | 44.8 -72 -407 -424 -501 -583 -828 -889 | 0 3 High 5 High 2 High 1 Low 2 High 1 High 3 Low |
| Massacre Shale | 995 | 1002 | -952 | 7 Low |
| Timboon Sandstone | 1016 | 1022 | -972 | 6 Low |
| Paaratte Formation | 1129 | 1128 | -1078 | 1 High |
| Skull Creek Formation | 1521 |  |  |  |
| Nullawarre Formation | 1712 |  |  |  |
| Belfast Mudstone | 1715 |  |  |  |
| Flaxmans Formation | 2026 |  |  |  |
| Waarre Formation Unit "C" | 2045 |  |  |  |
| Waarre Formation Unit "B" | 2075 |  |  |  |
| Waarre Formation Unit "A" | 2091 |  |  |  |
| Eumeralla Formation | 2131 |  |  |  |
| Total Depth | 2250 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1247-1323 | PAARATTE FORMATION Claystone (50%) interbedded with and grading to Sandstone (50%). CLAYSTONE: medium to dark grey to medium to dark brown grey to dark green grey, moderately to very silty, often very fine to finely arenaceous, trace dispersed medium to pebble sized quartz grains, trace fine black coaly detritus, trace pyrite, trace micromica, soft, non fissile. SANDSTONE: light to medium grey, very fine to fine, dominantly very fine, abundant dispersed medium to pebble quartz grains, subangular to rounded, poorly sorted, weak silica cement, abundant medium grey argillaceous and silt matrix, clear to opaque quartz grains, trace fine black coaly detritus, trace biotite flakes. trace pyrite, friable, very poor visual porosity, no oil fluorescence. |