WELL NAME: CRC No.1 PERMIT: PPL 13 DAILY GEOLOGICAL REPORT No. 13 DATE: 27/02/2007

Depth: 1723m Progress: 197m Days from Spud: 13

Rig: Century Rig No.11 GL(AHD): 44.8m Drilling Rep: Kevin Murphy/Brian Assels RT: (datum) 50.0m Geologist: David Horner Last Casing: 194mm at 512m

0600 hrs Update: Drill ahead with 171mm hole at 1771m. Nullawarre Formation - not present, top Belfast Mudstone picked at 1728m, however pick reliability is poor due to the gradational nature of the change in cuttings samples from definite Skull Creek to definite Belfast. Current lithology dark grey claystone (100%), background gas 0.023% (C1 97%, C2 3%, C3+ 0).

Comments: Drill ahead with 171mm hole to 1723m.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1528-1728 | Skull Creek Formation - No Show | TG 0.001-0.01% C1 97% C2 3% C3+ 0 |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Port Campbell Limestone Gellibrand Marl Clifton Formation Narrawaturk Marl Mepunga Formation Dilwyn Formation Pember Mudstone Pebble Point Formation | 5.2 125 462 476 550 635 879 936 | 5.2 122 457 474 551 633 878 939 | 44.8 -72 -407 -424 -501 -583 -828 -889 | 0 3 High 5 High 2 High 1 Low 2 High 1 High 3 Low |
| Massacre Shale | 995 | 1002 | -952 | 7 Low |
| Timboon Sandstone | 1016 | 1022 | -972 | 6 Low |
| Paaratte Formation | 1129 | 1128 | -1078 | 1 High |
| Skull Creek Formation | 1521 | 1528 | -1478 | 7 Low |
| Nullawarre Formation | 1712 | n/p | n/p | n/p |
| Belfast Mudstone | 1715 | 1728 | -1678 | 13 Low |
| Flaxmans Formation | 2026 |  |  |  |
| Waarre Formation Unit "C" | 2045 |  |  |  |
| Waarre Formation Unit "B" | 2075 |  |  |  |
| Waarre Formation Unit "A" | 2091 |  |  |  |
| Eumeralla Formation | 2131 |  |  |  |
| Total Depth | 2250 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1528-1728 | SKULL CREEK FORMATION Claystone (95%) laminated in part with Sandstone (5%) CLAYSTONE: light to dark grey to medium brown grey, often very silty, occasional abundant dispersed very fine quartz and altered feldspar grains, trace to common black coaly detritus and carbonaceous flecks, trace medium brown cryptocrystalline dolomite in part, trace pyrite, trace micromica, firm, slightly subfissile. SANDSTONE: off white to light grey, very fine, subangular to subrounded, moderately sorted, weak silica cement, abundant off white argillaceous matrix, quartzose with abundant altered feldspar grains, trace black coaly detritus, friable, very poor inferred porosity, no oil fluorescence. |