WELL NAME: CRC No.1 PERMIT: PPL 13 DAILY GEOLOGICAL REPORT No. 17 DATE: 03/03/2007

Depth: 1904m Progress: 3m Days from Spud: 17

Rig: Century Rig No.11 GL(AHD): 44.8m Drilling Rep: Kevin Murphy/Brian Assels RT: (datum) 50.0m Geologist: David Horner Last Casing: 194mm at 512m

0600 hrs Update: RIH, trip gas 0.14%, drill ahead with 171mm hole to 1976m. Current lithology, 100% Claystone (Belfast Mudstone), background gas 0.10%-0.19% (C1 93.6%, C2 6%, C3 0.4%, C4+ 0).

Comments: Cut Core No.3, 1900.0-1904.2m (4.2m), Recovered 1900.00-1902.65m (2.65m) 63%, Lay out core, RIH with new 4 blade PDC drill bit.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1901-1904 | Belfast Mudstone - No Show | TG 0.01-0.02% C1 97% C2 3% C3+ 0 |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Port Campbell Limestone Gellibrand Marl Clifton Formation Narrawaturk Marl Mepunga Formation Dilwyn Formation Pember Mudstone Pebble Point Formation | 5.2 125 462 476 550 635 879 936 | 5.2 122 457 474 551 633 878 939 | 44.8 -72 -407 -424 -501 -583 -828 -889 | 0 3 High 5 High 2 High 1 Low 2 High 1 High 3 Low |
| Massacre Shale | 995 | 1002 | -952 | 7 Low |
| Timboon Sandstone | 1016 | 1022 | -972 | 6 Low |
| Paaratte Formation | 1129 | 1128 | -1078 | 1 High |
| Skull Creek Formation | 1521 | 1528 | -1478 | 7 Low |
| Nullawarre Formation | 1712 | n/p | n/p | n/p |
| Belfast Mudstone | 1715 | 1728 | -1678 | 13 Low |
| Flaxmans Formation | 2026 |  |  |  |
| Waarre Formation Unit "C" | 2045 |  |  |  |
| Waarre Formation Unit "B" | 2075 |  |  |  |
| Waarre Formation Unit "A" | 2091 |  |  |  |
| Eumeralla Formation | 2131 |  |  |  |
| Total Depth | 2250 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1901-1904 | BELFAST MUDSTONE Massive Claystone (100%). CLAYSTONE: dark grey, slightly silty, moderately carbonaceous, trace black carbonaceous flecks, trace dark green glauconite, rare medium brown cryptocrystalline dolomite, trace Inocaramus, common micromica, moderately hard, slightly subfissile. |