WELL NAME: CRC No.1 PERMIT: PPL 13 DAILY GEOLOGICAL REPORT No. 6 DATE: 20/02/2007

Depth: 745m Progress: 229m Days from Spud: 6

Rig: Century Rig No.11 GL(AHD): 44.8m Drilling Rep: Kevin Murphy/Brian Assels RT: (datum) 50.0m Geologist: David Horner Last Casing: 194mm at 512m

0600 hrs Update: Drill ahead with 171mm hole at 836m. Current lithology: Dilwyn Formation, Sandstone (80%) interbedded with and grading to Claystone (20%), background gas 0.002-0.005%, C1 100%.

Comments: Adjust mast over hole, drill out shoe track and new 171mm hole to 519m, circulate hole clean, perform extended leakoff test to 13.3ppg mudweight equivalent, displace hole to new mud, drill ahead with 171mm hole to 745m. NOTE: Revised "Prognosed Formation Tops".

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 516-551 | Narrawaturk Marl - No Show | TG 0.001-0.002% C1 100% C2+ 0 |
| 551-633 | Mepunga Formation - No Show | TG 0.001-0.003% C1 100% C2+ 0 |
| 633-745 | Dilwyn Formation - No Show | TG 0.001-0.004% C1 100% C2+ 0 |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Port Campbell Limestone Gellibrand Marl Clifton Formation Narrawaturk Marl Mepunga Formation Dilwyn Formation Pember Mudstone Pebble Point Formation | 5.2 125 462 476 550 635 879 936 | 5.2 122 457 474 551 633 | 44.8 -72 -407 -424 -501 -583 | 0 3 High 5 High 2 High 1 Low 2 High |
| Massacre Shale | 995 |  |  |  |
| Timboon Sandstone | 1016 |  |  |  |
| Paaratte Formation | 1129 |  |  |  |
| Skull Creek Formation | 1521 |  |  |  |
| Nullawarre Formation | 1712 |  |  |  |
| Belfast Mudstone | 1715 |  |  |  |
| Flaxmans Formation | 2026 |  |  |  |
| Waarre Formation Unit "C" | 2045 |  |  |  |
| Waarre Formation Unit "B" | 2075 |  |  |  |
| Waarre Formation Unit "A" | 2091 |  |  |  |
| Eumeralla Formation | 2131 |  |  |  |
| Total Depth | 2250 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 516-551 | NARRAWATURK MARL Massive Marl (100%). MARL: medium to dark brown grey, trace to common green black glauconite, common fossil fragments, rare disseminated pyrite, soft, sticky, non fissile. |
| 551-633 | MEPUNGA FORMATION Claystone (60%) interbedded with and grading to Sandstone (40%). CLAYSTONE: off white to yellow to dark brown to dark brown grey, slightly to moderately silty, moderately to very calcareous, common to abundant dispersed very fine to grit brown iron oxide stained quartz grains, common glauconite, trace very fine black carbonaceous detritus, soft, moderately dispersive, non fissile. SANDSTONE: light yellow to dominantly medium brown, very fine to grit, dominantly coarse, subrounded to rounded, very poorly sorted, abundant off white to yellow to dark brown argillaceous matrix - grades to sandy claystone, abundant calcilutite matrix in part, weak to occasionally strong calcareous cement, brown iron oxide stained frosted quartz grains, trace to common dark brown iron oxide pellets, trace glauconite, unconsolidated to occasionally moderately hard, poor to fair visual porosity, no oil fluorescence. |
| 633-715 | DILWYN FORMATION Sandstone (70%) interbedded with and grading to Claystone (30%). SANDSTONE: light brown grey to medium brown, very fine to very coarse, dominantly medium, subangular to subrounded, poorly sorted, weak silica cement, abundant dark brown grey argillaceous matrix, clear to opaque quartz grains often with brown staining, trace marcasite, unconsolidated to friable, poor inferred porosity, no oil fluorescence. CLAYSTONE: dark brown to dark brown grey, moderately silty, common dispersed very fine to fine quartz sand grains in part, trace marcasite, moderately dispersive, soft, non fissile. |
| 715-745 | DILWYN FORMATION Sandstone (90%) interbedded with and grading to Claystone (10%). SANDSTONE: very light brown grey, very fine to very coarse, dominantly coarse, subangular to subrounded, poorly sorted, weak silica cement, common dark brown grey argillaceous matrix, clear to opaque quartz grains occasionally with yellow staining, trace coarse muscovite flakes, trace black coal detritus, trace marcasite, friable, good inferred porosity, no oil fluorescence. CLAYSTONE: medium brown to dark brown grey, moderately silty, common dispersed very fine to fine quartz sand grains in part, trace coarse muscovite flakes, trace marcasite, moderately dispersive, soft, non fissile. |