WELL NAME: CRC No.1 PERMIT: PPL 13 DAILY GEOLOGICAL REPORT No. 8 DATE: 22/02/2007

Depth: 1109m Progress: 194m Days from Spud: 8

Rig: Century Rig No.11 GL(AHD): 44.8m Drilling Rep: Kevin Murphy/Brian Assels RT: (datum) 50.0m Geologist: David Horner Last Casing: 194mm at 512m

0600 hrs Update: Drill ahead with 171mm hole to 1169m. Current lithology claystone (80%) laminated with very fine sandstone (20%), background gas 0.002% (C1 100%). Top Paaratte Formation at 1128m (1m High).

Comments: Cut Core No.1, 915.0-918.5m (3.5m), barrel jammed, POOH with Core No.1, recovered 915.0-917.03m (58%), RIH, trip gas 0.002% (C1 100%), drill ahead with 171mm hole to 1109m.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 915-939 | Pember Mudstone - No Show | TG 0.001-0.002% C1 100% C2+ 0 |
| 939-1002 | Pebbble Point Formation - No Show | TG 0.001-0.003% C1 100% C2+ 0 |
| 1002-1022 | Massacre Shale - No Show | TG 0.001-0.003% C1 100% C2+ 0 |
| 1022-1109 | Timboon Sandstone - No Show | TG 0.001-0.003% C1 100% C2+ 0 |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Port Campbell Limestone Gellibrand Marl Clifton Formation Narrawaturk Marl Mepunga Formation Dilwyn Formation Pember Mudstone Pebble Point Formation | 5.2 125 462 476 550 635 879 936 | 5.2 122 457 474 551 633 878 939 | 44.8 -72 -407 -424 -501 -583 -828 -889 | 0 3 High 5 High 2 High 1 Low 2 High 1 High 3 Low |
| Massacre Shale | 995 | 1002 | -952 | 7 Low |
| Timboon Sandstone | 1016 | 1022 | -972 | 6 Low |
| Paaratte Formation | 1129 |  |  |  |
| Skull Creek Formation | 1521 |  |  |  |
| Nullawarre Formation | 1712 |  |  |  |
| Belfast Mudstone | 1715 |  |  |  |
| Flaxmans Formation | 2026 |  |  |  |
| Waarre Formation Unit "C" | 2045 |  |  |  |
| Waarre Formation Unit "B" | 2075 |  |  |  |
| Waarre Formation Unit "A" | 2091 |  |  |  |
| Eumeralla Formation | 2131 |  |  |  |
| Total Depth | 2250 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 915-939 | PEMBER MUDSTONE Massive Claystone (100%). CLAYSTONE: dark brown grey to occasionally dark green grey, very silty, very finely arenaceous with angular to subangular clear to opaque quartz grains, trace fine brown and clear mica flakes, trace glauconite, common disseminated marcasite, soft, non fissile. |
| 939-1002 | PEBBLE POINT FORMATION Sandstone (50%) interbedded with and grading to Claystone (50%). SANDSTONE: medium orange brown, very fine to granular, dominantly coarse, subangular to subrounded, very poorly sorted, weak silica cement, abundant medium brown argillaceous and silt matrix, quartzose with yellow brown staining on quartz grains, rare iron oxide pellets, friable, fair to good inferred porosity, no oil fluorescence, grading to: SANDSTONE: light to brown, very fine to coarse, dominantly medium, subangular to subrounded, poorly sorted, weak silica cement, abundant dark brown grey argillaceous and silt matrix, clear to opaque quartz grains occasionally with brown staining, friable, very poor to poor inferred porosity, no oil fluorescence. CLAYSTONE: dark brown grey, moderately to very silty, abundant dispersed very fine to coarse quartz sand grains, soft, non fissile. |
| 1002-1022 | MASSACRE SHALE Massive Claystone (100%). CLAYSTONE: medium brown to dark brown grey, moderately to very silty, trace dispersed very fine to medium quartz sand grains, trace marcasite, soft, non fissile. |
| 1022-1109 | TIMBOON SANDSTONE Sandstone (50%) grading to Claystone (50%). SANDSTONE: light grey to light brown grey, very fine to grit, dominantly very fine and very coarse, angular to subrounded, very poorly sorted, weak silica cement, abundant off white to medium grey to dark brown grey argillaceous and silt matrix, clear to opaque quartz grains, trace yellow stained quartz grains, friable, poor inferred porosity, no oil fluorescence. CLAYSTONE: off white to medium grey, medium to dark brown grey, moderately to very silty, often abundant dispersed very fine to very coarse quartz sand grains, trace pyrite, soft, non fissile. |