WELL NAME: CRC No.1 PERMIT: PPL 13 DAILY GEOLOGICAL REPORT No. 9 DATE: 23/02/2007

Depth: 1245m Progress: 136m Days from Spud: 9

Rig: Century Rig No.11 GL(AHD): 44.8m Drilling Rep: Kevin Murphy/Brian Assels RT: (datum) 50.0m Geologist: David Horner Last Casing: 194mm at 512m

0600 hrs Update: RIH with coring assembly for Core No.2

Comments: Drill ahead with 171mm hole to 1240m, circulate geological sample, drill ahead to 1245m, wiper trip, POOH for Core No.2.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1109-1128 | Timboon Sandstone - No Show | TG 0.001-0.003% C1 100% C2+ 0 |
| 1128-1245 | Paaratte Formation - No Show | TG 0.001-0.003% C1 100% C2+ 0 |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Port Campbell Limestone Gellibrand Marl Clifton Formation Narrawaturk Marl Mepunga Formation Dilwyn Formation Pember Mudstone Pebble Point Formation | 5.2 125 462 476 550 635 879 936 | 5.2 122 457 474 551 633 878 939 | 44.8 -72 -407 -424 -501 -583 -828 -889 | 0 3 High 5 High 2 High 1 Low 2 High 1 High 3 Low |
| Massacre Shale | 995 | 1002 | -952 | 7 Low |
| Timboon Sandstone | 1016 | 1022 | -972 | 6 Low |
| Paaratte Formation | 1129 | 1128 | -1078 | 1 High |
| Skull Creek Formation | 1521 |  |  |  |
| Nullawarre Formation | 1712 |  |  |  |
| Belfast Mudstone | 1715 |  |  |  |
| Flaxmans Formation | 2026 |  |  |  |
| Waarre Formation Unit "C" | 2045 |  |  |  |
| Waarre Formation Unit "B" | 2075 |  |  |  |
| Waarre Formation Unit "A" | 2091 |  |  |  |
| Eumeralla Formation | 2131 |  |  |  |
| Total Depth | 2250 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1109-1128 | TIMBOON SANDSTONE Sandstone (80%) grading to Claystone (20%). SANDSTONE: light grey to light brown grey, very fine to grit, dominantly coarse, angular to subrounded, very poorly sorted, weak silica cement, abundant off white to medium grey to dark brown grey argillaceous and silt matrix, clear to opaque quartz grains, trace yellow stained quartz grains, trace black coal detritus, trace pyrite, friable, good inferred porosity, no oil fluorescence. CLAYSTONE: off white to medium grey to medium to dark brown grey, moderately to very silty, often abundant dispersed very fine to grit quartz sand grains, trace black coal detritus, trace pyrite, soft, non fissile. |
| 1128-1245 | PAARATTE FORMATION Claystone (80%) grading to and laminated with Sandstone (20%) CLAYSTONE: medium grey to medium brown grey, trace medium brown, moderately to very silty, often very fine to finely arenaceous, trace fine black coaly detritus, trace pyrite, soft, non fissile. SANDSTONE: light grey to light brown grey, very fine to fine, abundant dispersed medium to very coarse grains in part, dominantly very fine, subangular to subrounded, moderately sorted, weak silica cement, abundant off white to light grey argillaceous and silt matrix, clear to opaque quartz grains, trace fine black coaly detritus, trace pyrite, friable, very poor to poor visual porosity, no oil fluorescence. |