| WELL: | Childers Cove-1 | REPORT No.: | 2 | DAYS FROM SPUD: | 2 | DATE: | 20/09/05 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0000hrs Depth: | 547 | Last Depth: | 84 | 24 HR PROGRESS: | 463 | PTD: | 2536.0mRT(1) |
| 0600 OPS: | 21/09/05 –550m – Drilled to CSG TD, conduct wiper trip, and circulating after wiper trip preparing to POH. |
| REMARKS: | Geoservices was/is able to monitor drilling and tripping, although computer problems created the data unable to be stored. Thus, drill parameters and tripping details were monitored by computer, but recorded by hand. Geoservices H/O will rectify this inconvenience before drilling 8 ½” main hole. |

| PRIMARY OBJECTIVES: | Prognosed | SECONDARY OBJECTIVES: | Prognosed |
| --- | --- | --- | --- |
| Flaxman/Waarre Formation | 2349.0 m R.T. |  |  |
| Spud Date: | 18:00hrs 19/09/05 | Surface Latitude: | 38°29’31.96” | T.D. = |  | Metres R.T. |
| TD Reached Date: |  | Surface Longitude: | 142°44’46.66” | G.L. = | 46.2 | Metres ASL |
| Rig release Date: |  | Surface E (MGA94): | 0 652 295.0 | R.T. = | 51.5 | Metres ASL |
| Rig | Century Rig-7 | Surface N (MGA94): | 5 738 126.0 |  |  |
| Nearby Wells / Facilities are | 244mm Casing Shoe = |  | Metres R.T. |
|  | 178mm Casing Shoe = |  | Metres R.T. |

| Fm. Tops | Wellsite | Wellsite | Prognosed Depth | Diff | H/L |  | Sub-Sea Depth Comparisons |
| --- | --- | --- | --- | --- | --- | --- | --- |
| (* Geophysical Picks) | (mRT) | (mSS) | (mRT) | (mSS) |  |  |  | P-1ST1 | Diff | H/L |
| Port Campbell Limestone | 5.3 | 46.2 | 5.3 | 46.2 |  |  |  | 5.3 |  |  |
| Gellibrand Marl | 213.0 | -161.5 | 144.5 | -93.0 | 68.5 | L |  | -149.2 | 12.3 | L |
| Clifton Formation |  |  | 562.5 | -511.0 |  |  |  | -526.8 |  |  |
| Narrawaturk Marl |  |  | 592.5 | -541.0 |  |  |  | -546.2 |  |  |
| Mepunga Formation |  |  | 661.5 | -610.0 |  |  |  | -664.0 |  |  |
| Dilwyn Formation |  |  | 750.5 | -699.0 |  |  |  | -717.4 |  |  |
| Pember Mudstone |  |  | 1136.5 | -1085.0 |  |  |  | -936.3 |  |  |
| Pebble Point Formation |  |  | 1195.5 | -1144.0 |  |  |  | -1021.1 |  |  |
| Paaratte Formation |  |  | 1285.5 | -1234.0 |  |  |  | -1175.2 |  |  |  |  |  |  |  |  |  |
| Skull Creek Mudstone |  |  | 1756.5 | -1705.0 |  |  |  | -1643.7 |  |  |
| Nullawarre Green |  |  | 1922.5 | -1871.0 |  |  |  | -1740.2 |  |  |
| Belfast Mudstone |  |  | 2028.5 | -1977.0 |  |  |  | -1757.0 |  |  |
| Top Amplitudes |  |  | 2345.5 | -2294.0 |  |  |  | -1965.8 |  |  |
| Base Amplitudes |  |  | 2482.5 | -2431.0 |  |  |  | - |  |  |
| TD CDL-7 (shallow) |  |  | 2532.5 | -2481.0 |  |  |  | - |  |  |
| Eumeralla Formation |  |  | 2703.5 | -2652.0 |  |  |  | -2028.2 |  |  |
| TD CDL-7 (success case) |  |  | 2743.5 | -2692.0 |  |  |  | - |  |  |

Tops are wellsite picks

| Interval | ROP (ave) | Lithology Description |
| --- | --- | --- |
| Spud | - | 213.0 | 0.3-5.4 (1.5) | Massive LIMESTONE with trace MARL at later depths. LIMESTONE, off white, yellowish grey, pale olive, minor medium light grey, sparitic, micritic, common to abundant shell and coral fragments, trace green lithics, trace pyrite nodules, crystalline, microcrystalline in part, unconsolidated, friable to moderately hard. MARL, light to occasional medium grey, common shell and coral fragments, trace pyrite nodules, soft to dispersive, amorphous. |
| Gas | Units: | Nil | Composition (%): | - | / | - | / | - | / | - | / | - |
| Show Details / %CO2 | Nil |

| Interval | ROP (ave) | Lithology Description |
| --- | --- | --- |
| 213.0 | - | 550.0 | * | Massive MARL. MARL, light to medium grey, light olive grey, slightly greenish grey, argillaceous, calcareous, minor micro carbonaceous specks, very soft to soft, predominantly dispersive, rare firm in part, blocky to sub-blocky, dominantly amorphous. |
| Gas | Units: | Nil | Composition (%): | - | / | - | / | - | / | - | / | - |
| Show Details / %CO2 | Nil |

* Lost digital data due to computer problems, analog data not prepared by time of reporting.