| WELL: | Childers Cove-1 | REPORT No.: | 3 | DAYS FROM SPUD: | 3 | DATE: | 21/09/05 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0000hrs Depth: | 550 | Last Depth: | 547 | 24 HR PROGRESS: | 3 | PTD: | 2536.0mRT(1) |
|  |  |  |  |  |  |  | 2747.0mRT(2) |
| 0600 OPS: | 22/09/05 –551m – Continue dressing casing to weld on well head. |
| REMARKS: |  |

| PRIMARY OBJECTIVES: | Prognosed | SECONDARY OBJECTIVES: | Prognosed |
| --- | --- | --- | --- |
| Flaxman/Waarre Formation | 2349.0 m R.T. |  |  |
| Spud Date: | 18:00hrs 19/09/05 | Surface Latitude: | 38°29’31.96” | T.D. = |  | Metres R.T. |
| TD Reached Date: |  | Surface Longitude: | 142°44’46.66” | G.L. = | 46.2 | Metres ASL |
| Rig release Date: |  | Surface E (MGA94): | 0 652 295.0 | R.T. = | 51.5 | Metres ASL |
| Rig | Century Rig-7 | Surface N (MGA94): | 5 738 126.0 |  |  |
| Nearby Wells / Facilities are | 244mm Casing Shoe = |  | Metres R.T. |
|  | 178mm Casing Shoe = |  | Metres R.T. |

| Fm. Tops | Wellsite | Wellsite | Prognosed Depth | Diff | H/L |  | Sub-Sea Depth Comparisons |
| --- | --- | --- | --- | --- | --- | --- | --- |
| (* Geophysical Picks) | (mRT) | (mSS) | (mRT) | (mSS) |  |  |  | P-1ST1 | Diff | H/L |
| Port Campbell Limestone | 5.3 | 46.2 | 5.3 | 46.2 |  |  |  | 5.3 |  |  |
| Gellibrand Marl | 213.0 | -161.5 | 144.5 | -93.0 | 68.5 | L |  | -149.2 | 12.3 | L |
| Clifton Formation |  |  | 562.5 | -511.0 |  |  |  | -526.8 |  |  |
| Narrawaturk Marl |  |  | 592.5 | -541.0 |  |  |  | -546.2 |  |  |
| Mepunga Formation |  |  | 661.5 | -610.0 |  |  |  | -664.0 |  |  |
| Dilwyn Formation |  |  | 750.5 | -699.0 |  |  |  | -717.4 |  |  |
| Pember Mudstone |  |  | 1136.5 | -1085.0 |  |  |  | -936.3 |  |  |
| Pebble Point Formation |  |  | 1195.5 | -1144.0 |  |  |  | -1021.1 |  |  |
| Paaratte Formation |  |  | 1285.5 | -1234.0 |  |  |  | -1175.2 |  |  |  |  |  |  |  |  |  |
| Skull Creek Mudstone |  |  | 1756.5 | -1705.0 |  |  |  | -1643.7 |  |  |
| Nullawarre Green |  |  | 1922.5 | -1871.0 |  |  |  | -1740.2 |  |  |
| Belfast Mudstone |  |  | 2028.5 | -1977.0 |  |  |  | -1757.0 |  |  |
| Top Amplitudes |  |  | 2345.5 | -2294.0 |  |  |  | -1965.8 |  |  |
| Base Amplitudes |  |  | 2482.5 | -2431.0 |  |  |  | - |  |  |
| TD CDL-7 (shallow) |  |  | 2532.5 | -2481.0 |  |  |  | - |  |  |
| Eumeralla Formation |  |  | 2703.5 | -2652.0 |  |  |  | -2028.2 |  |  |
| TD CDL-7 (success case) |  |  | 2743.5 | -2692.0 |  |  |  | - |  |  |

Tops are wellsite picks

| Interval | ROP (ave) | Lithology Description |
| --- | --- | --- |
| Gas | Units: | Nil | Composition (%): | - | / | - | / | - | / | - | / | - |
| Show Details / %CO2 | Nil |