| WELL: | Childers Cove-1 | REPORT No.: | 8 | DAYS FROM SPUD: | 8 | DATE: | 26/09/05 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0000hrs Depth: | 1742 | Last Depth: | 1327 | 24 HR PROGRESS: | 415 | PTD: | 2536.0mRT(1) |
| 0600 OPS: | 27/09/05 – 1815m – Drilling 8 ½” main hole in the Skull Creek Mudstone. |
| REMARKS: |  |

| PRIMARY OBJECTIVES: | Prognosed | SECONDARY OBJECTIVES: | Prognosed |
| --- | --- | --- | --- |
| Flaxman/Waarre Formation | 2349.0 m R.T. |  |  |
| Spud Date: | 18:00hrs 19/09/05 | Surface Latitude: | 38°29’31.96” | T.D. = |  | Metres R.T. |
| TD Reached Date: |  | Surface Longitude: | 142°44’46.66” | G.L. = | 46.2 | Metres ASL |
| Rig release Date: |  | Surface E (MGA94): | 0 652 295.0 | R.T. = | 51.5 | Metres ASL |
| Rig | Century Rig-7 | Surface N (MGA94): | 5 738 126.0 |  |  |
| Nearby Wells / Facilities are | 244mm Casing Shoe = |  | Metres R.T. |
|  | 178mm Casing Shoe = |  | Metres R.T. |

| Fm. Tops | Wellsite | Wellsite | Prognosed Depth | Diff | H/L |  | Sub-Sea Depth Comparisons |
| --- | --- | --- | --- | --- | --- | --- | --- |
| (* Geophysical Picks) | (mRT) | (mSS) | (mRT) | (mSS) |  |  |  | P-1ST1 | Diff | H/L |
| Port Campbell Limestone | 5.3 | 46.2 | 5.3 | 46.2 |  |  |  | 5.3 |  |  |
| Gellibrand Marl | 213.0 | -161.5 | 144.5 | -93.0 | 68.5 | L |  | -149.2 | 12.3 | L |
| Clifton Formation | 595.5 | -544.0 | 562.5 | -511.0 | 33.0 | L |  | -526.8 | 17.2 | L |
| Narrawaturk Marl | 623.0 | -571.5 | 592.5 | -541.0 | 30.5 | L |  | -546.2 | 25.3 | L |
| Mepunga Formation | 645.0 | -593.5 | 661.5 | -610.0 | 16.5 | H |  | -664.0 | 70.3 | H |
| Dilwyn Formation | 775.0 | -723.5 | 750.5 | -699.0 | 24.5 | L |  | -717.4 | 6.1 | L |
| Pember Mudstone | 1191.0 | -1139.5 | 1136.5 | -1085.0 | 54.5 | L |  | -936.3 | 203.2 | L |
| Pebble Point Formation | 1225.0 | -1173.5 | 1195.5 | -1144.0 | 29.5 | L |  | -1021.1 | 152.4 | L |
| Paaratte Formation | 1287.0 | -1235.5 | 1285.5 | -1234.0 | 1.5 | L |  | -1175.2 | 60.3 | L |  |  |  |  |  |  |  |
| Skull Creek Mudstone | 1757.0 | -1705.5 | 1756.5 | -1705.0 | 0.5 | L |  | -1643.7 | 61.8 | L |
| Nullawarre Green |  |  | 1922.5 | -1871.0 |  |  |  | -1740.2 |  |  |
| Belfast Mudstone |  |  | 2028.5 | -1977.0 |  |  |  | -1757.0 |  |  |
| Top Amplitudes |  |  | 2345.5 | -2294.0 |  |  |  | -1965.8 |  |  |
| Base Amplitudes |  |  | 2482.5 | -2431.0 |  |  |  | - |  |  |
| TD CDL-7 (shallow) |  |  | 2532.5 | -2481.0 |  |  |  | - |  |  |
| Eumeralla Formation |  |  | 2703.5 | -2652.0 |  |  |  | -2028.2 |  |  |
| TD CDL-7 (success case) |  |  | 2743.5 | -2692.0 |  |  |  | - |  |  |

Tops are wellsite picks

| Interval | ROP (ave) | Lithology Description |
| --- | --- | --- |
| 1287.0 | - | 1670.0 | 0.5-44.6 (1.9) | Interbedded SANDSTONE and SILTSTONE. SANDSTONE, translucent to clear, frosted, opaque to milky in part, medium to coarse, common very coarse, occasional fine, sub-angular to sub-rounded, occasional angular, moderately sorted, weak siliceous cement, trace nod pyrite, carbonaceous fragments, loose and clean, good inferred porosity, no fluorescence. SILTSTONE, medium to dark grey, grayish brown, argillaceous, minor to common carbonaceous specks, occasional disseminated pyrite, trace glauconite, soft, dispersive in part, rare firm, sub-blocky to blocky, common amorphous. |
| Gas | Units: | Tr | Composition (%): | 100 | / | 0 | / | 0 | / | 0 | / | 0 |
| Show Details / %CO2 | Nil |

| Interval | ROP (ave) | Lithology Description |
| --- | --- | --- |
| 1670.0 | - | 1757.0 | 0.9-46.5 (3.3) | SILTSTONE with interbedded SANDSTONE. SANDSTONE, clear, translucent, light grey to colourless, predominantly medium to fine, rare coarse grains, predominantly sub-angular. Minor sub-rounded, weak siliceous cement, no visual matrix, trace pyrite, common carbonaceous specks, loose, hard to very hard in part, fair inferred and poor to fair visual porosity, no fluorescence. SILTSTONE, medium to dark grey, light grey, arenaceous, argillaceous in part, occasional carbonaceous specks and flecks, minor disseminated pyrite, soft to dispersive, blocky to amorphous. |
| Gas | Units: | Tr-3 | Composition (%): | 95 | / | 5 | / | 0 | / | 0 | / | 0 |
| Show Details / %CO2 | Nil |

| 1757.0 | - | (1815.0) | 1.3-9.0 (2.9) | SILTSTONE with interbedded SANDSTONE. SANDSTONE, translucent to clear, pale grey to off white, very fine to fine, well sorted, trace weak calcareous cement, abundant off white pale grey argillaceous and kaolinite matrix, trace carbonaceous specks, trace nod pyrite, friable, poor visual porosity, no fluorescence. SILTSTONE, medium to dark grey, grayish brown, light grey, argillaceous, minor arenaceous, rare glauconite, micromicaceous, trace carbonaceous specks, very soft to dispersive, dominantly amorphous, blocky in part. |
| --- | --- | --- | --- | --- |
| Gas | Units: | Tr-4 | Composition (%): | 96 | / | 4 | / | 0 | / | 0 | / | 0 |
| Show Details / %CO2 | Nil |