| WELL: | Childers Cove-1 | REPORT No.: | 9 | DAYS FROM SPUD: | 9 | DATE: | 27/09/05 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0000hrs Depth: | 2058 | Last Depth: | 1742 | 24 HR PROGRESS: | 316 | PTD: | 2536.0mRT(1) |
| 0600 OPS: | 28/09/05 – 2152m – Drilling 8 ½” main hole in the Belfast Mudstone. |
| REMARKS: |  |

| PRIMARY OBJECTIVES: | Prognosed | SECONDARY OBJECTIVES: | Prognosed |
| --- | --- | --- | --- |
| Flaxman/Waarre Formation | 2349.0 m R.T. |  |  |
| Spud Date: | 18:00hrs 19/09/05 | Surface Latitude: | 38°29’31.96” | T.D. = |  | Metres R.T. |
| TD Reached Date: |  | Surface Longitude: | 142°44’46.66” | G.L. = | 46.2 | Metres ASL |
| Rig release Date: |  | Surface E (MGA94): | 0 652 295.0 | R.T. = | 51.5 | Metres ASL |
| Rig | Century Rig-7 | Surface N (MGA94): | 5 738 126.0 |  |  |
| Nearby Wells / Facilities are | 244mm Casing Shoe = | 544.5 | Metres R.T. |
|  | 178mm Casing Shoe = |  | Metres R.T. |

| Fm. Tops | Wellsite | Wellsite | Prognosed Depth | Diff | H/L |  | Sub-Sea Depth Comparisons |
| --- | --- | --- | --- | --- | --- | --- | --- |
| (* Geophysical Picks) | (mRT) | (mSS) | (mRT) | (mSS) |  |  |  | P-1ST1 | Diff | H/L |
| Port Campbell Limestone | 5.3 | 46.2 | 5.3 | 46.2 |  |  |  | 5.3 |  |  |
| Gellibrand Marl | 213.0 | -161.5 | 144.5 | -93.0 | 68.5 | L |  | -149.2 | 12.3 | L |
| Clifton Formation | 595.5 | -544.0 | 562.5 | -511.0 | 33.0 | L |  | -526.8 | 17.2 | L |
| Narrawaturk Marl | 623.0 | -571.5 | 592.5 | -541.0 | 30.5 | L |  | -546.2 | 25.3 | L |
| Mepunga Formation | 645.0 | -593.5 | 661.5 | -610.0 | 16.5 | H |  | -664.0 | 70.3 | H |
| Dilwyn Formation | 775.0 | -723.5 | 750.5 | -699.0 | 24.5 | L |  | -717.4 | 6.1 | L |
| Pember Mudstone | 1191.0 | -1139.5 | 1136.5 | -1085.0 | 54.5 | L |  | -936.3 | 203.2 | L |
| Pebble Point Formation | 1225.0 | -1173.5 | 1195.5 | -1144.0 | 29.5 | L |  | -1021.1 | 152.4 | L |
| Paaratte Formation | 1287.0 | -1235.5 | 1285.5 | -1234.0 | 1.5 | L |  | -1175.2 | 60.3 | L |  |  |  |  |  |  |  |
| Skull Creek Mudstone | 1757.0 | -1705.5 | 1756.5 | -1705.0 | 0.5 | L |  | -1643.7 | 61.8 | L |
| Nullawarre Green | 1919.5 | -1868.0 | 1922.5 | -1871.0 | 2.0 | H |  | -1740.2 | 127.8 | L |
| Belfast Mudstone | 2027.0 | -1975.5 | 2028.5 | -1977.0 | 1.5 | H |  | -1757.0 | 218.5 | L |
| Top Amplitudes |  |  | 2345.5 | -2294.0 |  |  |  | -1965.8 |  |  |
| Base Amplitudes |  |  | 2482.5 | -2431.0 |  |  |  | - |  |  |
| TD CDL-7 (shallow) |  |  | 2532.5 | -2481.0 |  |  |  | - |  |  |
| Eumeralla Formation |  |  | 2703.5 | -2652.0 |  |  |  | -2028.2 |  |  |
| TD CDL-7 (success case) |  |  | 2743.5 | -2692.0 |  |  |  | - |  |  |

Tops are wellsite picks

| Interval | ROP (ave) | Lithology Description |
| --- | --- | --- |
| 1757.0 | - | 1919.5 | 1.0-30.9 (2.5) | SILTSTONE with interbedded SANDSTONE. SANDSTONE, translucent to clear, pale grey to off white, very fine to fine, well sorted, trace weak calcareous cement, abundant off white pale grey argillaceous and kaolinite matrix, trace carbonaceous specks, trace nodular pyrite, friable, poor visual porosity, no fluorescence. SILTSTONE, medium to dark grey, greyish brown, light grey, argillaceous, minor arenaceous, rare glauconite, micromicaceous, trace carbonaceous specks, very soft to dispersive, dominantly amorphous, blocky in part. |
| Gas | Units: | Tr-7 | Composition (%): | 98 | / | 2 | / | 0 | / | 0 | / | 0 |
| Show Details / %CO2 | Nil |

| Interval | ROP (ave) | Lithology Description |
| --- | --- | --- |
| 1919.5 | - | 2027.0 | 0.7-24.2 (3.1) | SILTSTONE with trace interbedded SANDSTONE. SANDSTONE, light yellowish grey, light orange, translucent, clear, colourless, very fine to medium, moderately to well sorted, trace siliceous cement, no visual matrix, glauconite, loose and clean, generally fair porosity, no fluorescence. SILTSTONE, light grey, light greenish grey, olive grey, light brownish grey, dominantly arenaceous, locally common argillaceous in part, trace glauconite, carbonaceous specks, dispersive in part, firm to minor moderately hard, blocky to sub-blocky, slightly sub-fissile in part, amorphous. |
| Gas | Units: | Tr-7 | Composition (%): | 97 | / | 3 | / | 0 | / | 0 | / | 0 |
| Show Details / %CO2 | Nil |

| 2027.0 | - | (2152) | 1.2-16.1 (2.1) | Massive SILTSTONE with minor SANDSTONE lenses and trace LIMESTONE. SANDSTONE, off white to brownish grey, very fine, occasional fine, generally very well sorted, sub-angular to sub-rounded, very weak calcareous cement, generally silty, abundant argillaceous matrix, common glauconite, unconsolidated, very poor to tight visual porosity, no fluorescence. SILTSTONE, predominantly grey to brownish grey, very argillaceous, grading to CLAYSTONE in part, localized common glauconite in part, trace carbonaceous material in part, generally soft to firm in part, slightly moderately calcareous, sub-fissile to sub-blocky. LIMESTONE, cream, minor argillaceous/fossiliferous, soft to brittle. |
| --- | --- | --- | --- | --- |
| Gas | Units: | 1-9 | Composition (%): | 96 | / | 4 | / | 0 | / | 0 | / | 0 |
| Show Details / %CO2 | Nil |