| WELL: | Childers Cove-1 | REPORT No.: | 10 | DAYS FROM SPUD: | 10 | DATE: | 28/09/05 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0000hrs Depth: | 2246 | Last Depth: | 2058 | 24 HR PROGRESS: | 188 | PTD: | 2536.0mRT(1) |
| 0600 OPS: | 29/09/05 – 2246m – RIH after wiper trip to shoe, drill 8 ½” main hole in the Belfast Mudstone. |
| REMARKS: |  |

| PRIMARY OBJECTIVES: | Prognosed | SECONDARY OBJECTIVES: | Prognosed |
| --- | --- | --- | --- |
| Flaxman/Waarre Formation | 2349.0 m R.T. |  |  |
| Spud Date: | 18:00hrs 19/09/05 | Surface Latitude: | 38°29’31.96” | T.D. = |  | Metres R.T. |
| TD Reached Date: |  | Surface Longitude: | 142°44’46.66” | G.L. = | 46.2 | Metres ASL |
| Rig release Date: |  | Surface E (MGA94): | 0 652 295.0 | R.T. = | 51.5 | Metres ASL |
| Rig | Century Rig-7 | Surface N (MGA94): | 5 738 126.0 |  |  |
| Nearby Wells / Facilities are | 244mm Casing Shoe = | 544.5 | Metres R.T. |
|  | 178mm Casing Shoe = |  | Metres R.T. |

| Fm. Tops | Wellsite | Wellsite | Prognosed Depth | Diff | H/L |  | Sub-Sea Depth Comparisons |
| --- | --- | --- | --- | --- | --- | --- | --- |
| (* Geophysical Picks) | (mRT) | (mSS) | (mRT) | (mSS) |  |  |  | P-1ST1 | Diff | H/L |
| Port Campbell Limestone | 5.3 | 46.2 | 5.3 | 46.2 |  |  |  | 5.3 |  |  |
| Gellibrand Marl | 213.0 | -161.5 | 144.5 | -93.0 | 68.5 | L |  | -149.2 | 12.3 | L |
| Clifton Formation | 595.5 | -544.0 | 562.5 | -511.0 | 33.0 | L |  | -526.8 | 17.2 | L |
| Narrawaturk Marl | 623.0 | -571.5 | 592.5 | -541.0 | 30.5 | L |  | -546.2 | 25.3 | L |
| Mepunga Formation | 645.0 | -593.5 | 661.5 | -610.0 | 16.5 | H |  | -664.0 | 70.3 | H |
| Dilwyn Formation | 775.0 | -723.5 | 750.5 | -699.0 | 24.5 | L |  | -717.4 | 6.1 | L |
| Pember Mudstone | 1191.0 | -1139.5 | 1136.5 | -1085.0 | 54.5 | L |  | -936.3 | 203.2 | L |
| Pebble Point Formation | 1225.0 | -1173.5 | 1195.5 | -1144.0 | 29.5 | L |  | -1021.1 | 152.4 | L |
| Paaratte Formation | 1287.0 | -1235.5 | 1285.5 | -1234.0 | 1.5 | L |  | -1175.2 | 60.3 | L |  |  |  |  |  |  |  |
| Skull Creek Mudstone | 1757.0 | -1705.5 | 1756.5 | -1705.0 | 0.5 | L |  | -1643.7 | 61.8 | L |
| Nullawarre Green | 1919.5 | -1868.0 | 1922.5 | -1871.0 | 2.0 | H |  | -1740.2 | 127.8 | L |
| Belfast Mudstone | 2027.0 | -1975.5 | 2028.5 | -1977.0 | 1.5 | H |  | -1757.0 | 218.5 | L |
| Top Amplitudes |  |  | 2345.5 | -2294.0 |  |  |  | -1965.8 |  |  |
| Base Amplitudes |  |  | 2482.5 | -2431.0 |  |  |  | - |  |  |
| TD CDL-7 (shallow) |  |  | 2532.5 | -2481.0 |  |  |  | - |  |  |
| Eumeralla Formation |  |  | 2703.5 | -2652.0 |  |  |  | -2028.2 |  |  |
| TD CDL-7 (success case) |  |  | 2743.5 | -2692.0 |  |  |  | - |  |  |

Tops are wellsite picks

| Interval | ROP (ave) | Lithology Description |
| --- | --- | --- |
| 2027.0 | - | (2246) | 1.2-16.1 (2.1) | Massive SILTSTONE with minor SANDSTONE lenses and trace LIMESTONE. SANDSTONE, off white to brownish grey, very fine, occasional fine, generally very well sorted, sub-angular to sub-rounded, very weak calcareous cement, generally siliceous, abundant argillaceous matrix, common glauconite, unconsolidated, very poor to tight visual porosity, n/p. SILTSTONE, predominantly grey to brownish grey, very argillaceous, grading to CLAYSTONE in part, localized common glauconite in part, trace carbonaceous material in part, generally soft to firm in part, slightly moderately calcareous, sub-fissile to sub-blocky. LIMESTONE, cream, minor argillaceous/fossiliferous, soft to brittle. |
| Gas | Units: | 1-9 | Composition (%): | 96 | / | 4 | / | Tr | / | 0 | / | 0 |
| Show Details / %CO2 | Nil |