| WELL: | Childers Cove-1 | REPORT No.: | 15 | DAYS FROM SPUD: | 15 | DATE: | 03/10/05 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0000hrs Depth: | 2658 | Last Depth: | 2616 | 24 HR PROGRESS: | 42 | PTD: | 2536.0mRT(1) |
| 0600 OPS: | 04/10/05 – 2658m – RIH with P & A programme |
| REMARKS: | Childers Cove-1 reached a TD of 2658mRT at 08:00hors on 3rd October, 2005. |

| PRIMARY OBJECTIVES: | Prognosed | SECONDARY OBJECTIVES: | Prognosed |
| --- | --- | --- | --- |
| Flaxman/Waarre Formation | 2349.0 m R.T. |  |  |
| Spud Date: | 18:00hrs 19/09/05 | Surface Latitude: | 38°29’31.96” | T.D. = | 2658.0 | Metres R.T. |
| TD Reached Date: | 08:00hrs 03/10/05 | Surface Longitude: | 142°44’46.66” | G.L. = | 46.2 | Metres ASL |
| Rig release Date: |  | Surface E (MGA94): | 0 652 295.0 | R.T. = | 51.5 | Metres ASL |
| Rig | Century Rig-7 | Surface N (MGA94): | 5 738 126.0 |  |  |
| Nearby Wells / Facilities are | 244mm Casing Shoe = | 544.5 | Metres R.T. |
|  | 178mm Casing Shoe = | N/A | Metres R.T. |

| Fm. Tops | Wellsite | Wellsite | Prognosed Depth | Diff | H/L |  | Sub-Sea Depth Comparisons |
| --- | --- | --- | --- | --- | --- | --- | --- |
| (* Geophysical Picks) | (mRT) | (mSS) | (mRT) | (mSS) |  |  |  | P-1ST1 | Diff | H/L |
| Port Campbell Limestone | 5.3 | 46.2 | 5.3 | 46.2 |  |  |  | 5.3 |  |  |
| Gellibrand Marl | 213.0 | -161.5 | 144.5 | -93.0 | 68.5 | L |  | -149.2 | 12.3 | L |
| Clifton Formation | 595.5 | -544.0 | 562.5 | -511.0 | 33.0 | L |  | -526.8 | 17.2 | L |
| Narrawaturk Marl | 623.0 | -571.5 | 592.5 | -541.0 | 30.5 | L |  | -546.2 | 25.3 | L |
| Mepunga Formation | 659.0 | -593.5 | 661.5 | -610.0 | 16.5 | H |  | -664.0 | 70.3 | H |
| Dilwyn Formation | 743.4 | -723.5 | 750.5 | -699.0 | 24.5 | L |  | -717.4 | 6.1 | L |
| Pember Mudstone | 1056.3 | -1139.5 | 1136.5 | -1085.0 | 54.5 | L |  | -936.3 | 203.2 | L |
| Pebble Point Formation | 1137.3 | -1173.5 | 1195.5 | -1144.0 | 29.5 | L |  | -1021.1 | 152.4 | L |
| Paaratte Formation | 1237.4 | -1235.5 | 1285.5 | -1234.0 | 1.5 | L |  | -1175.2 | 60.3 | L |
| Skull Creek Mudstone | 1746.0 | -1705.5 | 1756.5 | -1705.0 | 0.5 | L |  | -1643.7 | 61.8 | L |
| Nullawarre Green | 1926.0 | -1868.0 | 1922.5 | -1871.0 | 2.0 | H |  | -1740.2 | 127.8 | L |
| Belfast Mudstone | 2013.9 | -1975.5 | 2028.5 | -1977.0 | 1.5 | H |  | -1757.0 | 218.5 | L |
| Top Amplitudes | 2318.7 | -2283.5 | 2345.5 | -2294.0 | 10.5 | L |  | -1965.8 | 317.7 | L |
| Base Amplitudes | 2471.0 | -2419.5 | 2482.5 | -2431.0 | 11.5 | H |  | - |  |  |
| TD CDL-7 (shallow) | 2545.0 | -2493.5 | 2532.5 | -2481.0 | 12.5 | L |  | - |  |  |
| Eumeralla Formation | 2435.0 | -23838. | 2703.5 | -2652.0 | 268.5 | H |  | -2028.2 | 401.3 | L |
| TD CDL-7 (success case) | 2658 | -2606.5 | 2743.5 | -2692.0 | 85.5 | H |  | - |  |  |

Tops are wellsite picks

Wireline picks

| 2622.0 | - | 2658.0 TD | 3.3-38.1 (10.5) | Massive TUFF. TUFF, light greenish grey, off white, trace greenish red, trace yellowish orange, very argillaceous, very calcareous in part, common chlorite in part, common dispersive, very soft, occasional slightly firm in part, abundant amorphous, rare sub-blocky aggregates. |
| --- | --- | --- | --- | --- |
| Gas | Units: | 6-17 | Composition (%): | 95 | / | 4 | / | 1 | / | 0 | / | 0 |
| Show Details / %CO2 | Nil |