Report for : Richard Moore / Greg Doty / Sam Falkner

Compiled by : Mark Smith

| WELL | CBA A19A |
| --- | --- |
| DATE | 29-04-2009 |
| REPORT # | 16 |
| MIDNIGHT ACTIVITY | Making up 7" casing shoe hanger. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 3200.0 mMDRT |  | MINIMUM | - | - |
| TVD | 2473.4 mTVDRT |  | MAXIMUM | - | - |
| PROGRESS LAST 24 hrs | 0.0 m |  | AVERAGE | - | - |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.0m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Top Lakes Entrance |  |  |  |  | 2829.0 | 2206.0 |
| Top of Latrobe Group |  |  |  |  | 3049.0 | 2365.6 |
| Top Coarse Clastics / M111 reservoir |  |  |  |  | 3053.7 | 2370.1 |
| Top M112 reservoir |  |  |  |  | 3063.1 | 2375.4 |
| Top M131 Upper reservoir |  |  |  |  | 3071.4 | 2381.1 |
| Top M132 Upper reservoir |  |  |  |  | 3094.4 | 2396.9 |
| Top M132 Lower reservoir |  |  |  |  | 3105.2 | 2404.2 |
| 3.5FS |  |  |  |  | 3105.2 | 2405.2 |
| M141 reservoir |  |  |  |  | 3111.3 | 2408.5 |
| Halibut Original Oil Water Contact |  |  |  |  | 3154.2 | 2438.0 |
| Total Depth | 3200.00 | 2473.45 | 2432.45 |  | 3194.2 | 2465.2 |

| Current Formation | Latrobe Group |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | - | - | - | - | - | - | - | - |
| MAX (GFF) | - | - | - | - | - | - | - | - |
| BG (Reserval) | - | - | - | - | - | - | - | - |
| BG (GFF) | - | - | - | - | - | - | - | - |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 4RR | 3 |
| SIZE (in) | 8½ | 8½ |
| MANUFACTURER/TYPE | REED HYCALOG RSX616M | REED HP21G |
| JETS (/32 inch) | 6 x 18 | 3 x 18 |
| DEPTH IN (m) | 732.0 | 615.0 |
| DEPTH OUT (m) | 3200.0 | 732.0 |
| METRES ON RUN (m) | 2468.0 | 117.0 |
| HRS ON BTM 24hrs/total | 55.2 | 11.1 |
| BIT CONDITION | 3-3-CT-S/N-X-In-WT-TD | 1-1-WT-A-E-E-E-In-No-BHA |
| RPM RANGE 24hrs |  |  |
| Pump Hrs 24 hrs / total | 9.3 / 101.1 | 22.0 |
| Krevs 24 hrs / total | 991 | 208 |

| 24 HOUR SUMMARY | Back ream out of hole from 1943.0 mMDRT to 860.0 mMDRT. Pump out of hole from 860.0 mMDRT to 830.0 mMDRT, 30 klbs overpull at 855.0 mMDRT. Wash back in hole to 860.0 mMDRT. Back ream out of hole from 860.0 mMDRT to 594.0 mMDRT. Circulate hole clean from 594.0 mMDRT to 566.0 mMDRT, flow check and pump slug. Function test BOPs and conduct Koomey unit test. Pull out of hole from 566.0 mMDRT to BHA at 235.0 mMDRT. Flow check and pull out with HWDP to 37.0 mMDRT. Pull out of hole with 8½" rotary steerable drilling assembly, unload source, lay out tools and break bit. Clean and clear rig floor. Retrieve wear bushing and jet stack. Rig up Weatherford casing gear on rig floor. Make up casing hanger as per Cameron instructions. |
| --- | --- |
| 30-04-2009 5AM UPDATE | Continue to make up casing hanger as per Cameron instructions and lay out. Install Weatherford FMS slips. Make up shoe track and check float. Run in hole with 7" casing from 12.0 mMDRT to 543.0 mMDRT. 5AM DEPTH: 3200.00 mMDRT (2473.45 mTVDRT) |