Report for : Richard Moore / Greg Doty / Sam Falkner

Compiled by : Mark Smith

| WELL | CBA A19A |
| --- | --- |
| DATE | 30-04-2009 |
| REPORT # | 17 |
| MIDNIGHT ACTIVITY | Pick up and make up casing hanger at 3172.0 mMDRT. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 3200.0 mMDRT |  | MINIMUM | - | - |
| TVD | 2473.4 mTVDRT |  | MAXIMUM | - | - |
| PROGRESS LAST 24 hrs | 0.0 m |  | AVERAGE | - | - |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.0m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Top Lakes Entrance |  |  |  |  | 2829.0 | 2206.0 |
| Top of Latrobe Group |  |  |  |  | 3049.0 | 2365.6 |
| Top Coarse Clastics / M111 reservoir |  |  |  |  | 3053.7 | 2370.1 |
| Top M112 reservoir |  |  |  |  | 3063.1 | 2375.4 |
| Top M131 Upper reservoir |  |  |  |  | 3071.4 | 2381.1 |
| Top M132 Upper reservoir |  |  |  |  | 3094.4 | 2396.9 |
| Top M132 Lower reservoir |  |  |  |  | 3105.2 | 2404.2 |
| 3.5FS |  |  |  |  | 3105.2 | 2405.2 |
| M141 reservoir |  |  |  |  | 3111.3 | 2408.5 |
| Halibut Original Oil Water Contact |  |  |  |  | 3154.2 | 2438.0 |
| Total Depth | 3200.00 | 2473.45 | 2432.45 |  | 3194.2 | 2465.2 |

| Current Formation | Latrobe Group |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | - | - | - | - | - | - | - | - |
| MAX (GFF) | - | - | - | - | - | - | - | - |
| BG (Reserval) | - | - | - | - | - | - | - | - |
| BG (GFF) | - | - | - | - | - | - | - | - |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. |  | 4RR |
| SIZE (in) |  | 8½ |
| MANUFACTURER/TYPE |  | REED HYCALOG RSX616M |
| JETS (/32 inch) |  | 6 x 18 |
| DEPTH IN (m) |  | 732.0 |
| DEPTH OUT (m) |  | 3200.0 |
| METRES ON RUN (m) |  | 2468.0 |
| HRS ON BTM 24hrs/total |  | 55.2 |
| BIT CONDITION |  | 3-3-CT-S/N-X-In-WT-TD |
| RPM RANGE 24hrs |  |  |
| Pump Hrs 24 hrs / total |  | 101.1 |
| Krevs 24 hrs / total |  | 991 |

| 24 HOUR SUMMARY | Continue to make up casing hanger as per Cameron instructions and lay out. Install Weatherford FMS slips. Make up shoe track and check float. Run in hole with 7" casing from 12.0 mMDRT to 592.0 mMDRT. Make up pump in sub, stage up to 5 bbl/min and circulate 1 times bottoms up. Run in hole with 7" casing from 529.0 mMDRT to 2206.0 mMDRT. Break circulation and increase pump rate to 5 bbls / min, while working casing string. Run in hole with 7" casing from 2206.0 mMDRT to 3172.0 mMDRT. Drain riser and stack back to pits. Pick up and make up casing hanger at 3172.0 mMDRT. |
| --- | --- |
| 01-05-2009 5AM UPDATE | Pick up and make up casing hanger at 3172.0 mMDRT. Run in hole with landing joint and land out hanger at 3196.0 mMDRT. Make up cement head and surface lines. Break circulation and stage up pumps to 5 bbl/min. Circulate casing volume prior to cement job. Halliburton mix and pump cement as per program. Displace cement with inhibited seawater with rig pumps. 5AM DEPTH: 3200.00 mMDRT (2473.45 mTVDRT) |