DATE: 24 March 2009						TIME:	 0535 hrs

CURRENT DEPTH:	3700.0 mMDRT / 2356.0 mTVDRT

BIT DEPTH:		2655.0 mMDRT

CURRENT OPERATION: RIH to drill ahead.

LAST SURVEY: 3655.62 mMDRT / 59.33° INC / 358.94 ° AZI / 2332.6 mTVDRT

DD (deviation from Line):  1.79 m Left / 2.02 m Above

ROP: (MIN/MAX/AVG) (m/hr): 0 / 0 / 0

GAS (Reserval Units):

Bkgd / Max :	0 / 0 units

Trip Gas =	-

MUD Weight:		11.85 ppg. (circulating weight)

GEOSERVICES:

- All systems OK.

ANADRILL:

- All systems OK.

- LWD tools changed out on surface. Back-up tools picked up and RIH.

- Memory from LWD tools read. Logs being prepared.

- Shallow hole tests conducted at 37m and 235m.

- A/C still functioning improperly. A/C technician due on rig on today.

LAST SAMPLE: 3699 mMDRT: 60% Calcareous Claystone, 35% Sandstone, 5% Siltstone

FORMATION: Latrobe Formation

GENERAL:

- Forward Plan: RIH, drill ahead 9-7/8” hole to TD.

- Estimated return to drilling before midday.

Daniel van der Aa / Justin Eastwood

Wellsite Geologists

CBA A21A