Report for : Richard Moore / Mark Calicutt / Andy Choy

Compiled by  : Col Chadwick

| WELL | CBA-A21A |
| --- | --- |
| DATE | 23-03-2009 |
| REPORT # | 09 |
| MIDNIGHT ACTIVITY | RIH @ 614.87 mMDRT |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 3700.0 mMDRT |  | MINIMUM |  |  |
| TVD | 2356.30 mTVDRT |  | MAXIMUM |  |  |
| PROGRESS LAST 24 hrs | 0 m |  | AVERAGE |  |  |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.0m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Lakes Entrance Fm. | 3390.0 | 2185.9 | -2144.9 | 12.1 H | 3406.0 | 2198.0 |
| Top of Latrobe Grp | 3665.5 | 2337.7 | -2296.7 | 7.7 L | 3648.0 | 2330.0 |
| Top Coarse Clastics / M111 Reservoir |  |  |  |  | 3656.0 | 2334.0 |
| Top M112 Reservoir |  |  |  |  | 3689.9 | 2351.0 |
| Top M131 Reservoir |  |  |  |  | 3699.9 | 2356.0 |
| Top M132 Upper Reservoir |  |  |  |  | 3733.8 | 2373.0 |
| Top M132 Lower Reservoir |  |  |  |  | 3741.8 | 2377.0 |
| 4AFS Marker |  |  |  |  | 3763.8 | 2388.0 |
| M145 Reservoir |  |  |  |  | 3791.7 | 2402.0 |
| Halibut Org OWC |  |  |  |  | 3863.5 | 2438.0 |
| Total Depth |  |  |  |  | 3903.5 | 2458.0 |

| Current Formation | 60% CLAYSTONE ; 5% SILTSTONE; 35% SANDSTONE |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | - | - | - | - | - | - | - | - |
| MAX (GFF) | - | - | - | - | - | - | - | - |
| BG (Reserval) | - | - | - | - | - | - | - | - |
| BG (GFF) | - | - | - | - | - | - | - | - |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 2 | 1 |
| SIZE (in) | 97/8" | 97/8" |
| MANUFACTURER/TYPE | Reed Hycalog RSX616M-A11 | Reed Hycalog RSX616M-A11 |
| JETS (/32 inch) | 6 x 18 | 6 x 18 |
| DEPTH IN (m) | 3700.0 | 638.0 |
| DEPTH OUT (m) | - | - |
| METRES ON RUN (m) | 0 | 3062.0 |
| HRS ON BTM 24hrs/total | 0 / 0 | / |
| BIT CONDITION | - | 8-8-RO-A-X-IN-HC-PR/PP |
| RPM RANGE 24hrs | / | / |
| Pump Hrs 24 hrs / total | 1.1 / 1.1 | 4.5 / 135.3 |
| Krevs 24 hrs / total | / | 7/ 590 |

| 24 HOUR SUMMARY | Continued to pull out of hole on elevators to 2241.0 mMDRT. Encountered tight spot at 2241.0 mMDRT and 2213.0 mMDRT. Work through. Pull out of hole on elevators from 2113.0 mMDRT to 1952.0 mMDRT. Run in hole from 1952.0 mMDRT to 2008.0 mMDRT. Pull out of hole from 1952.0 mMDRT to 1942.0 mMDRT. Hole packing off at 1942.0 mMDRT. No rotation. Worked pipe through and rotated at 30 rpm. Pumped out of hole from 1942.0 mMDRT to 1919.0 mMDRT. Pulled out of hole on elevators from 1919.0 mMDRT to 964.0 mMDRT. 40 Klbs overpull encountered at 964.0 mMDRT. Worked string, made up top-drive and established circulation and rotation and backreamed back into the shoe at 638.0 mMDRT. Circulated bottoms up. Flow checked and pulled out of hole 5.5” drill pipe on elevators from 638.0 mMDRT to 237.0 mMDRT. Flow checked and pulled out of hole 5.5” HWDP from 237.0 mMDRT to 37.0 mMDRT. Unloaded radio active source from logging tool and pulled out of hole BHA to surface. Laid out BHA. Make up New BHA and run in hole same to 37.0 mMDRT. Shallow hole tested Schlumberger MWD/LWD tools. Run in hole HWDP from 37.0 mMDRT to 235.0 mMDRT. Shallow hole tested Schlumberger MWD/LWD tools. Ran in hole 5.5” drill pipe from 235.0 mMDRT to 614.0 mMDRT. Rig service. |
| --- | --- |
| 24-03-2009 5AM UPDATE | Continued to run in hole 5.5” drill pipe from 614.0 mMDRT to 2421.0 mMDRT filling pipe every 15 stands. 3700.0 mMDRT (2356.30 mTVDRT) 2421.0 mMDRT Bit Depth |

NOTE: YESTERDAYS PUMP HOURS SHOULD HAVE READ: 17 / 130.8