Report for : Richard Moore / Mark Calicutt / Andy Choy

Compiled by  : Col Chadwick

| WELL | CBA-A21A |
| --- | --- |
| DATE | 24-03-2009 |
| REPORT # | 10 |
| MIDNIGHT ACTIVITY | BACKREAM OOH @ 3670.0 mMDRT |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 3923.0 mMDRT |  | MINIMUM | 2.05 | 3701.0 |
| TVD | 2467.70 mTVDRT |  | MAXIMUM | 81.38 | 3724.5 |
| PROGRESS LAST 24 hrs | 223.0 m |  | AVERAGE | 35.40 | 3700-3923m |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.0m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Lakes Entrance Fm. | 3390.0 | 2185.9 | -2144.9 | 12.1 H | 3406.0 | 2198.0 |
| Top of Latrobe Grp | 3665.5 | 2337.7 | -2296.7 | 7.7 L | 3648.0 | 2330.0 |
| Top Coarse Clastics / M111 Reservoir | 3668.0 | 2339.0 | -2298.0 | 5.0 L | 3656.0 | 2334.0 |
| Top M112 Reservoir | 3701.5 | 2355.0 | -2314.0 | 4.0 L | 3689.9 | 2351.0 |
| Top M131 Reservoir | 3716.0 | 2363.0 | -2322.0 | 7.0 L | 3699.9 | 2356.0 |
| Top M132 Upper Reservoir | 3746.0 | 2378.1 | -2337.1 | 5.1 L | 3733.8 | 2373.0 |
| Top M132 Lower Reservoir | 3755.0 | 2382.6 | -2341.6 | 5.6 L | 3741.8 | 2377.0 |
| 4AFS Marker | 3777.0 | 2393.8 | -2352.8 | 5.8 L | 3763.8 | 2388.0 |
| M145 Reservoir | 3812.0 | 2411.6 | -2370.0 | 9.0 L | 3791.7 | 2402.0 |
| Halibut Org OWC | 3846.4 | 2438.0 | -2397.0 | - | 3863.5 | 2438.0 |
| Total Depth | 2923.0 | 2467.7 | -2426.7 | 9.7L | 3903.5 | 2458.0 |

| Current Formation | 90% CLAYSTONE ; 10% SANDSTONE |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 3720.5 | 87.00 | 0.551 | 0.148 | 0.180 | 0.119 | 0.037 | - |
| MAX (GFF) |  |  |  |  |  |  |  | - |
| BG (Reserval) |  | 41.93 | 0.230 | 0.066 | 0.077 | 0.059 | 0.021 | - |
| BG (GFF) | - | - | - | - | - | - | - | - |
| TRIP GAS (Reserval) | 3884 | 33.40 | 0.103 | 0.038 | 0.054 | 0.056 | 0.025 | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

GFF SYSTEM PROBLEMS – DRILLING RATE TO QUICK TO FIX – NOW FIXED

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 2 | 1 |
| SIZE (in) | 97/8" | 97/8" |
| MANUFACTURER/TYPE | Reed Hycalog RSX616M-A11 | Reed Hycalog RSX616M-A11 |
| JETS (/32 inch) | 6 x 18 | 6 x 18 |
| DEPTH IN (m) | 3700.0 | 638.0 |
| DEPTH OUT (m) | - | 3700.0 |
| METRES ON RUN (m) | 223 | 3062.0 |
| HRS ON BTM 24hrs/total | 6.3 / 6.3 | 0 / 87.1 |
| BIT CONDITION |  | 8-8-RO-A-X-IN-HC-PR/PP |
| RPM RANGE 24hrs | 74 / 84.5 | / |
| Pump Hrs 24 hrs / total | 14.4 / 15.5 | 0 / 135.3 |
| Krevs 24 hrs / total | 47 / 47 | 0 / 590 |

| 24 HOUR SUMMARY | Continued to run in hole 5.5” drill pipe from 614.0 mMDRT to 3687.0 mMDRT filling pipe every 15 stands. Washed last stand to bottom from 3687.0 mMDRT to 3700.0 mMDRT. Drill, steer and survey 97/8" hole from 3700.0 mMDRT to 3923.0 mMDRT. Circulate 3 times bottoms up and condition mud racking back one stand per bottoms up from 3923.0 mMDRT to 3850.0 mMDRT. Backream out of hole from 3850.0 mMDRT to 3710.0 mMDRT. Anadrill log out of hole from 3710.0 mMDRT to 3695.0 mMDRT at 40m per hour. Backream out of hole from 3695.0 mMDRT to 3670.0 mMDRT. |
| --- | --- |
| 25-03-2009 5AM UPDATE | Backream out of hole from 3670.0 mMDRT to 3090.0 MMDRT. 3923.0 mMDRT (2467.70 mTVDRT) 3090.0 mMDRT Bit Depth |