Report for : Sam Falkner / Greg Doty / Richard Moore

Compiled by : Gareth Munro

| WELL | CBA A33 |
| --- | --- |
| DATE | 24-06-2009 |
| REPORT # | 11 |
| MIDNIGHT ACTIVITY | Break down BHA #4 |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 2579.00 mMDRT |  | MINIMUM | 14.31 | 2489.0 |
| TVD | 2502.15 mMDRT |  | MAXIMUM | 134.6 | 2338.5 |
| PROGRESS LAST 24 hrs | 250 m |  | AVERAGE | 47.17 |  |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.0m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Top Lakes Entrance | 2233.0 | 2168.2 | -2127.2 | 22.8mH | 2255.0 | 2191.0 |
| Top of Latrobe Group | 2462.0 | 2389.3 | -2348.3 | 5.7mH | 2466.0 | 2395.0 |
| Top Coarse Clastics | 2464.0 | 2391.2 | -2350.2 | 5.8mH | 2468.0 | 2397.0 |
| Top M112 Reservoir | 2479.0 | 2405.7 | -2364.7 | 2.3mH | 2480.0 | 2408.0 |
| Top M131A Reservoir | 2482.0 | 2408.6 | -2367.6 | 1.4mH | 2482.0 | 2410.0 |
| Top M131AB Reservoir | 2487.0 | 2413.4 | -2372.4 | 0.6mH | 2486.0 | 2414.0 |
| Top M132 | 2490.0 | 2416.3 | -2375.3 | 3.7mH | 2492.0 | 2420.0 |
| Top M141 | 2495.5 | 3421.6 | -2380.6 | 3.4mH | 2497.0 | 2425.0 |
| Original Oil Water Contact |  |  |  |  | 2512.0 | 2438.0 |
| Total Depth | 2579.00 | 2502.15 | -2461.15 |  | 2552.0 | 2478.2 |

| Current Formation | Latrobe Group |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 2470.0 | 159.0 | 0.703 | 0.234 | 0.339 | 0.245 | 0.083 | 0 |
| MAX (GFF) | 2470.0 | 90.0 | 0.485 | 0.167 | 0.267 | 0.215 | 0.065 | 0 |
| BG (Reserval) | 2329 - 2579 | 29.2 | 0.201 | 0.037 | 0.042 | 0.034 | 0.012 | - |
| BG (GFF) | 2329 - 2579 | 16.5 | 0.161 | 0.020 | 0.031 | 0.026 | 0.009 | - |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 4 | 3RR |
| SIZE (in) | 9.875 | 14.75 |
| MANUFACTURER/TYPE | Reed Hycalog, RSX616M | Reed Hycalog, P11 |
| JETS (/32 inch) | 3 x 14 / 3 x 16 | 2 x 24 |
| DEPTH IN (m) | 589.62 | 202.5 |
| DEPTH OUT (m) | 2579.00 | 589.62 |
| METRES ON RUN (m) | 1989.38 | 387 |
| HRS ON BTM 24hrs/total | 5.3 / 27.9 | 0 / 12.1 |
| BIT CONDITION | - | 1-1-WT-A-E-IN-NO-TD |
| RPM RANGE 24hrs | 102 -127 | - |
| Pump Hrs 24 hrs / total | 9.4 / 43.2 | 0 / 24.5 |
| Krevs 24 hrs / total | 35.9 / 210.4 | 0 / 40.9 |

| 24 HOUR SUMMARY | Circulate hole clean at 2370.0 mMDRT prior to entering the Latrobe Group, Baracarb added to mud system. Drill and survey 9-7/8” hole to 2494.0 mMDRT as per Anadrill’s instructions. Max ROP 50 m/hr. Drill and survey hole from 2516m to TD at 2579m as per Anadrill instructions. Max ROP 50 m/hr in pay zone. Circulate hole clean from 2579m to 2546m, racking back a stand every bottoms up. Downlink to tools and shoot survey. Flow check “OK”. Pull out of hole 5 ½” drill pipe from 2546m to 978m. Look for washes in string. Tight spots, 30k overpull seen, ream out of hole from 978m to 732m. “OK”. Ream string through tight spots at 978m, 829m and 741m. |
| --- | --- |
| 25-06-2009 5 AM UPDATE | Ream out of hole from 732m to inside shoe at 585m. Pull out of hole, break down and lay out bottom hole assembly. Pull wear bushing and jet stack. Rig service. Rig up Weatherford. AM DEPTH: 2579.0 mMDRT (2502.15 mTVDRT) |